Economical Digital Video/Audio Recorders

Quick Reference

DVR-Q61300E

Before Turning On The System

- Please install SATA HDDs in the Hard Disk bracket, and DVD Writer in the DVD bracket.  (Sec. 2.1, 3.1)

- Please set the NTSC/PAL Selector Switch according to the local TV system.  (Sec. 2.2)

- Please refer to Chapter 3 for all connections.

After Turning On The System

- Please wait for about 40 seconds for the system to start up.

- Please login the system (Sec. 4.2), and then physically format the HDDs (Sec. 6.6.1).  (Please note that the HDDs cannot be used for recording if they are not formatted yet.)

- Please refer to Sec. 6.8 and Appendix C to set the time zone of the system.

- Please refer to Section 4.1 to enter text.

- Please refer to Section 4.3 for all basic operations.

- Please refer to Chapter 6 to setup the system correctly, esp. Section 6.8 for Time Zone, DST & Language.

- Please refer to Chapter 8 to search, playback, and archive the recorded video/audio.

- Please refer to Sec. 2.2, 6.10, and Chapter 9 for remote access via internet or intranet.

- Please refer to Sec. 2.2, 6.1, 6.9, and Chapter 7 to control the PTZ cameras correctly.

- Please refer to Sec. 2.2, 3.2, 6.9, and Appendix D to use the keyboard controller or terminal correctly.

- Please refer to Sec. 2.2, 3.2, 6.9, 4.3, 8.6, and Appendix G to use GPS function correctly.

- Please refer to Sec. 2.2, 3.2, 6.9, 4.3, 8.5, 8.6, and 8.10 to use POS function correctly.

- Please refer to Appendix E or Recording-table.xls for the estimated recording time.

- Please refer to Appendix F for the bundled MS-Windows utilities.

- Please refer to Appendix H for the Protocol Converter for Multiple POS.

Special Note

- For internal DVD, please do not block the tray from ejecting while the DVD is in backup process.  Blocking the tray from ejecting may damage the DVD writer.

Login The System

- Login / Logout : MENU->Login/Logout

Setup The System

- Format HDD : MENU->Setup->HDD->Format HDD (MODE)->Physical Format (CALL)

- Change Time Zone, Language : MENU->Setup->System->Time Zone, Language

- Setup PTZ, Keyboard, POS, GPS : MENU->Setup->RS-232/422/485->Device Type, ..

- Setup Network : MENU->Setup->Network->Net Type, Static IP or PPPoE, ..

- Change Network Port : MENU->Setup->Network->Adv.

Basic Operations

- Change Split Window :  +/-

- Change Live / Playback mode : MODE

- Move Focus : ▲, ▼, ◄, ►

- Connect / Disconnect Backup Device : MENU->Backup Device->Connect / Disconnect

- Search/Playback/Archive : Search->Search By Time, Smart Search, ..

- Search By Time : Select the start time & video type, and

- Play : , MODE, Search

- Backup :

- Search By Event : Select and move to the event, and

- Play :

- Backup :

- Smart Search : Select the camera, area covered by the motion occurred, and start/end time, and press SEARCH or MODE to search the matched files.  Select and move to the file, and

- Play :

- Backup :

- Search Archived File : Connect Backup Device (by pressing ENTER in Device), and select and move to the file, and

- Play :

- POS Search : Select the camera, keyword, and start/end time, and press SEARCH or MODE to search the matched files.  Select and move to the file, and

- Play :

- Backup :

- Backup : Connect Backup Device (by pressing ENTER in Device), and select cameras, end time, etc., and

- Backup :

- Stop Backup :

Note: For internal DVD, please do not block the tray from ejecting while the DVD is in backup process.  Blocking the tray from ejecting may damage the DVD writer.

Remote Access -> Before Logging On

- Set the domain name or IP address of the DVR as trusted web site in your I.E., and the (https:) server verification for trusted web site as unchecked (Tools->Options->Security in I.E.).  For I.E. 7, please set the Security level for this zone to Low.

- If the PC has used I.E. to access earlier software version of DVR, please go to Tools->Options->General in your I.E. to delete “Temporary Internet files” and all offline contents.

Remote Access -> Operations

- Please note that the PC user must have system administrator password for the PC; otherwise, the process will fail, and an error dialog will be shown.

- Add More DVRs : Click on  to call up Setup dialog.  Add more DVRs in the DVR list.

- Select DVR : Click on one of  or .

- Context Menu : Right-click in the video window to call up Context Menu.