4CH MEPG4

Digital Hard Disk Recorder

( UDR-4004 )

Features:

- Real-time 4 channel standalone type

- Stable Operating System ( Embedded Linux )

- MPEG4 compression

- Real-time Recording Support

•4ch : 120fps at Full D1 (NTSC), 100fps at Full D1 (PAL)

- Quadplex mode for simultaneous recording, playback, backup, and network transmission

- Remote viewing, access and control, back up through the network

- Dynamic IP support ( DHCP & PPPoE ) and DDNS server available

- CMS (Central Monitoring Station ) supports up to 128 channels

- Monitoring by Internet explorer

- Alarm Triggered E-mail alert function

- Various Event Notification ( Video POP-UP, Icon, Buzzer, Relay Output )

- NTP (Network Time Protocol ) support

- Audio support through the network

- Supports various alarm events: Motion detection, External Sensors, & Video loss detection

- Various backup method support : USB(Ver2.0), Network

- Audio recording available (4CH)

- Multiple recording modes: Time lapse, pre/post alarm, scheduled, motion, manual, & continuous recording

- Pre alarm recording for 5sec. and Post alarm recording for 60sec

- Convenient search by calendar, event (motion, sensor)

- Quick and responsive playback & field-by-field viewing with keys and Remote Controller

- Slow Play Function ( x1/2, x1/4 )

- Water mark function ( backup )

- PTZ control through RS-485

- SATA HDD support

- Security password protection

- Easy software update via USB port and Network

- IR remote control & Mouse support

- Multi language support

- Dual video mode: Selectable NTSC & PAL

- Loop through output support with option cable (termination on/off control function)

- Free volt power input ( 100V - 240VAC, 50Hz / 60Hz ) using adaptor(12VDC)

| Model | 4ch DVR |
| --- | --- |
| Image System | NTSC, PAL selectable |
| Multi-tasking | Quadplex |
| Video Channel | 4CH Composite, BNC |
| Video Output | 1CH Composite BNC, 1CH VGA |
| Video Compression | MPEG4 |
| Recording Resolution | 704x480, 704x240, 352x240 (NTSC) / 704x576, 704x288, 352x288 (PAL) |
| Recording Quality | 4 Levels (Normal, Enhanced, Fine, Super Fine) |
| Max Display Speed | 120 fps (NTSC) / 100 fps (NTSC) |
| Max Recording Speed | 120 fps at Full D1 (NTSC) / 100 fps at Full D1 (PAL) |
| Time Laps Recording Interval (fps) | 1,2,3,4,5,6,7,8,9,10,15,20,30 (NTSC, 13 Steps) 1,2,3,4,5,6,7,8,9,10,15,20,25 (PAL, 13 Steps) |
| Recording Mode | Schedule, Event (Sensor, Motion Detection), Manual, Continuous, Continuous+Event |
| Playback Search | Calendar, Event (Sensor, Motion Detection) |
| Playback Speed | x1, x2, x4, x8, x16, x32, x64, x128, Field by Field (Forward, Backward) |
| Slow Motion | x1/4, x1/2 (Forward Only) |
| Sensor Input | 4 (NO/NC Selectable) |
| Alarm Output (Relay) | 1 (NO/NC) , 4 TTL Output |
| Audio In/Out | 4 Input / 1 Output |
| Network | 10/100Base-T (Static, DHCP, PPPoE, E-mail & FTP), DDNS server available |
| Motion Detection | 22x15 (NTSC) / 22x18 (PAL), 8 Level Sensitivity |
| Hard Disk | Max. 1 EA |
| Backup | USB(Ver2.0), Network |
| Watermarking | Still Image Backup |
| PTZ Control | RS-485 |
| System Log | Video Loss, Power On/Off, HDD Full, HDD Fail, Menu Called, Reset HDD Format, Reset SW Upgrade, Email Fail |
| Language | Korean, English, Japanese, French, Spanish, German, Polish, Italian, Russian, Slovak |
| S/W Upgrade | Network, USB Memory Stick |
| Password Function | Power OFF, MENU, Record OFF, Key Lock |
| Power Source | Free Voltage (100 –240VAC, 50Hz/60Hz) using adaptor(12VDC) |
| Dimension | 280mm(W) x 320mm(D) x 44mm(H) |
| Operating Temperature | 5℃ ~ 40℃ |
| Weight | 3.5Kg (net) |

- Design and specifications are subjected to change without notice.

4ch DVR

FRONT

REAR

# Text boxes

MPEG4 녹화 시험

MPEG4 Chip Device Driver 구현 및 시험

308 / 316 테스트용

B/D조립 및 시험

308 / 316 테스트용

PCB설계

308 / 316 1차 HMS회로 설계

308 / 316 1차 HMS PCB 설계

308 / 316 1차 HMS

예비인증시험

308 / 316 1차 HMS

B/D 조립 및 시험

Support 검토

충격흡수 Rubber검토

304 필름 진행

304 1차 HMS

회로 설계

304 1차 HMS

PCB 설계

RAMS 기능구현

Client 시험 ( CODEC )

달력 검색 기능

MPEG4 재생 시험

308 / 316 테스트용회로 설계