Matrix Keyboard controller

(Model No.: UKB-400)

How to connect the keyboard controller with UDR-400 series,

How to operate the keyboard with UDR-400 series

- How to connect with UDR-400 series DVR, How to connect with Speed dome

  - Connect DVR with Controller Junction box: Connect RS-485 A port of DVR with DVR port of Controller Junction box (Caution +/- polarity)

  - Connect Speed Dome with Controller Junction box: Connect RS-485 port of Speed Dome with CAM1 or CAM2 of Controller Junction box (Caution +/- polarity)

- DVR MENU setting (By using MENU on DVR)

  - Menu -> Camera Setup -> PTZ Setup ->

Model No : PELCO-D

PTZ ID : 0~255 (In case of “0”, it is normally not used)

Baud Rate: 2400

(Support only PELCO-D protocol when connect Controller)

  - Menu -> System Setup -> DVR ID -> 0 ~ 255(In case of “0”, it is normally not used)

- Keyboard Controller setting (No use to change it because it is set as the default)

  - Enter Setting mode : “1” +”1”+ ”SEL”  (Push “SEL” button in 3 seconds)

  - Camera control Baud rate : 1. Baud rate #1 : Master 2400

  - DVR control Baud rate : 2. Baud rate #2 : Slave 9600

  - Protocol : 3. Protocol : Tpro 201  (Same as PELCO-D)

  - Exit after saving the setting value : 8. Save and Exit

- Keyboard Controller operation

There are DVR mode and Camera model on Controller.

Change DVR mode : DVR ID + “DVR” button

Change Camera mode: CAMERA ID + “CAM” button or CAMERA ID + “MATRIX” button

  - How to operate DVR

    - Select DVR  : “ 1 ”(DVR ID) + “ DVR ” button

    - Example to operate

      - Menu setting screen ON/OFF : “ MENU ” button

      - Change Live screen : “ 0 “ + “ DISP “ : Same way by pushing “MULTI” button on DVR

    - DVR control command button: MENU, ZOOM, FRZ, SEQ, DISP, REC, R.PLAY, PLAY, PAUSE, STOP, SEARCH, ENTER, JOYSTICK

  - How to operate CAMERA

    - Select Camera : “ 1 ”(CAMERA ID) + “ CAM ” button

    - Example to operate

      - ZOOM TELE : “ ZOOM TELE ” button

      - IRIS OPEN : “ IRIS OPEN ” button

    - CAMERA control command button : ZOOM TELE, ZOOM WIDE, FOCUS NEAR, FOCUS FAR, IRIS OPEN, IRIS CLSE, PRST, PTRN, SCAN, JOYSTICK

  - How to operate Matrix function (When connect a lot of DVRs by using Daisy chain cable)

    - How to connect and how to set DVR, Daisy chain cable, Speed Dome Camera

      - Plug in optional Daisy chain cable into extension port on No.1, No.2 DVR.

      - Connect Daisy chain cable Vd_out on No.1 DVR into Daisy chain cable Vd_in on No.2 DVR

      - Connect Daisy chain cable Vd_out on No.2 DVR into monitor (Matrix output screen)

      - Set “1” on No.1 DVR ID and set “2” on No.2 DVR ID.

      - Set “1~16” on No.1 DVR that is connected with Speed Dome camera ID and set 17~32 on No.2 DVR that is connect with Speed Dome Camera ID.

    - Example to operate

      - Select No.17 Camera: “ 17 ” + “ MATRIX ” button

        - Watch No.1 camera screen of No.2 DVR on Matrix output screen. In this case, the camera control command can be operated because the keyboard controller is on the camera mode.