UKB-400

GENERAL DESCRIPTIONS

GENERAL DESCRIPTIONS

UKB-400 is DVR & Camera controller and it allows operator to use the functions easily.

* This keyboard controls DVR and Camera such as DVR setup, PB, PTZ function.

* The LCD shows display current status as well as provides a menu to set operational parameters.

* This controller is designed for desktop operation and interface connectors are located in the junction box.

FEATURES

* To control all DVR function such as Live display, Playback, DVR Setup, PTZ and Matrix.

* To control up to 255 DVRs from one key board.

* To control up to 255 cameras from one key board.

* Multi-protocol supported ( PELCO-D, VICON ).

* Preset position control.

* Maximum speed is changed according to zoom ratio.

* To recall programmed auto-scan from selected dome camera

* Built in LCD Display with blue screen.

* User password and system hold function

SPECIFICATION

| MODEL | UKB-400 |
| --- | --- |
| Communication | MASTER(for CAM) : RS-485 (2400bps, 4800bps, 9600bps) SLAVE(for DVR) : RS-485 (2400bps, 4800bps, 9600bps) |
| Joystick | Axis | 3-Axis, Zoom IN/OUT available |
|  | Power Consumption | DC 12V, 110mA |
| Display Type | 16 x 2 Character LCD, With Blue Backlight |
| Key Type | PC Key board Button |
| Key board Connector Type | RJ45 8 Pin Modular Cable |
| Junction Box Connector | Master : Terminal Block. Slave : Terminal Block |
| Humidity | 10% ~ 70% non Condensing |
| Dimension | 140(W) x 185(H) x 365(D) |
| Weight | 1.2kg |

DIMENSION