MERX HTTP API

Version 1.0.0

# Preface

This document details the API of MERX video products. Programmers can access and configure MERX video products follows the API.

# Catalog

1. Preface	2

2. Catalog	2

3. HTTP API Transaction	5

3.1Transaction	5

3.2Authentication	6

4. Camera	7

4.1 Stream	7

4.1.1 GetStream	7

4.2 CameraCap	7

4.2.1 GetCameraConfig	7

4.2.2 SetCameraConfig	8

4.3 VideoColor	10

4.3.1 GetVideoColorConfig	10

4.3.2 SetVideoColorConfig	11

4.3.3 Resolution	11

5. Live	12

5.1 Live General	12

5.1.1 GetLiveGeneralConfig	12

5.1.2 SetLiveGeneralConfig	12

5.2 OSD	13

5.2.1 GetOSDConfig	13

5.2.2 SetOSDConfig	13

5.3 VideoCover	14

5.3.1 GetVideoCoverConfig	14

5.3.2 SetVideoCoverConfig	14

6. Stream	15

6.1 MainStream	15

6.1.1 GetMainStreamConfig	15

6.1.2 SetMainStreamConfig	16

6.2 Sub Stream	18

6.2.1 GetSubStreamConfig	18

6.2.2 SetSubStreamConfig	18

6.3 Mobile Stream	21

6.3.1 GetMobileStreamConfig	21

6.3.2 SetMobileStreamConfig	21

6.4 Audio	23

6.4.1 GetAudioConfig	23

6.4.2 SetAudioConfig	24

7. NetWork	24

7.1 BasicConfig	24

7.1.1 GetBasicConfig	24

7.1.2 SetBasicConfig	25

7.2 3G	26

7.2.1 Get3GConfig	26

7.2.2 Set3GConfig	26

7.3 Wifi	27

7.3.1 GetWifiConfig	27

7.3.2 SetWifiConfig	27

7.4 DDNS	28

7.4.1 GetDDNSConfig	28

7.4.2 SetDDNSConfig	29

7.5 Email	29

7.5.1 GetEmailConfig	29

7.5.2 SetEmailConfig	30

7.6 P2P	31

7.6.1 GetP2PConfig	31

7.6.2 SetP2PConfig	31

7.7 RTSP	31

7.7.1 GetRTSPConfig	31

7.7.2 SetRTSPConfig	32

7.8 FTP	32

7.8.1 GetFTPConfig	32

7.8.2 SetFTPConfig	33

7.9 Platform	34

7.9.1 GetPlatformConfig	34

7.9.2 SetPlatformConfig	34

7.10 Mobile	35

7.10.1 GetMobileConfig	35

7.10.2 SetMobileConfig	35

7.11 GB28181	35

7.11.1 GetGB28181Config	35

7.11.2 SetGB28181Config	36

8. Alarm	37

8.1 IO Alarm	37

8.1.1 GetIOAlarmConfig	37

8.1.2 SetIOAlarmConfig	37

8.2 MotionDetect	38

8.2.1 GetMotionDetectConfig	38

8.2.2 SetMotionDetectConfig	38

8.3 PerimeterLine	40

8.3.1 GetPerimeterLineConfig	40

8.3.2 SetPerimeterLineConfig	40

8.4 OSCAlarm	41

8.4.1 GetOSCAlarm	41

8.4.2 SetOSCAlarm	42

8.5 ODAlarm	43

8.5.1 GetODAlarm	43

8.5.2 SetODAlarm	43

9. Record & Snap	44

9.1 General Record	44

9.1.1 GetGeneralRecConfig	44

9.1.2 SetGeneralRecConfig	45

9.2 Smart Record	45

9.2.1 GetSmartRecConfig	45

9.2.2 SetSmartRecConfig	45

9.3 Schedule	46

9.3.1 GetScheduleConfig	46

9.3.2 SetScheduleConfig	46

9.4 Snap	47

9.4.1 GetSnapConfig	47

9.4.2 SetSnapConfig	47

10. System	48

10.1 General	48

10.1.1 GetSysGeneralConfig	48

10.1.2 SetSysGeneralConfig	48

10.2 User	49

10.2.1 GetUserConfig	49

10.2.2 SetUserConfig	49

10.3 NTP	50

10.3.1 GetNTPConfig	50

10.3.2 SetNTPConfig	50

10.4 DST	52

10.4.1 GetDSTConfig	52

10.4.2 SetDSTConfig	52

11. Storage	53

11.1 CloudStorage	53

11.1.1 GetCloudStorageConfig	53

11.1.2 SetCloudStorageConfig	54

11.2 Storage Device	54

11.2.1 GetDevStorageConfig	54

11.2.2 SetDevStorageConfig	55

12. Advance	55

12.1 IP Filter	55

12.1.1 GetIPFilterConfig	55

12.1.2 SetIPFilterConfig	55

12.2 FtpUpgrade	56

12.2.1 GetFtpUpgradeConfig	56

12.2.2 SetFtpUpgradeConfig	56

13. Events	57

13.1 EventHandler	57

13.1.1 GetEventHandler	57

# HTTP API Transaction

## 3.1Transaction

The HTTP API Transaction starts from a request from a client Application, usually a web browser. The request is processed by the web server on the MERX video products, then send the response back to the client application. The HTTP request is taken in GET form. If the request is successful, the MERX video product will return a HTTP header contains 200 OK. The HTTP Body will contain actual data or error message if an error occurs.

For describe convenience, we use some short words to instead the long expressions. The follows are several regulations:

- The italics and bold will be replaced by the value behind the symbol “=”.

- The URL must follow the standard way of writing a URL.(RFC_3986:Uniform Resource Identifiers (URI) Generic Syntax);that is ,spaces and other reserved characters (“;”, “/”, “?”, “:”, “@”, “=”, “+”, “,” and “$”) within a <paramName> or a <paramValue> must be replaced with %<ASCII hex>.For example ,the blank must be instead with %20.

- To describe the range of the configuration, we use some symbols such as “[]”, “{}” and so on. For example :”[0-100]” denotes a integer not less than 0 and not larger than 100. “{0,1,2,3}” denotes the valid value of a integer among 0,1,2 and 3.

- In the request and response, we use “[]” to denote an array. The index is usually a integer and start form 0.

- The parameter value has several types: string, integer, bool and float.Integer is 32 bits.The range of bool is “true” and “false”.

The below is an example of a transaction:

| Request | GET http://<ip>/action/getConfig?name=VideoColor |
| --- | --- |
| Description | Get VideoColor configuration. |
| Response | HTTP/1.1 200 OK Content-Type:text/plain Brightness=50 Contrast=50 Hue=50 Saturation=50 |
| Comment | ...... We can also request the single config. For example: Request : GET http://10.7.2.4/action/getConfig?name=VideoColor.Brightness Response: HTTP/1.1 200 OK Content-Type:text/plain VideoColor.Brightness=50 |

## 3.2Authentication

The MERX video product supplies two authentication ways: basic authentication and digest authentication. If the http request does not have  “Authorization” , the MERX video product returns 401, utill the http request has a legal authentication .

For example:

1. When basic authentication, the MERX video product response:

401 Unauthorized

WWW-Authenticate: Basic realm=”XXXXXX”

Then the client encode the username and password with base64, send the following request:

Authorization: Basic VXZVXZ.

2. When digest authentication, the MERX video product response:

WWW-Authenticate: Digest realm="MERX.cn", nonce="7a86c864b7fadff5457f90ec803a9182", qop="auth";

The client calculates the digest using username, password, nonce, realm and URI with MD5, then send the following request:

Authorization: Digest username="admin", realm="MERX.cn", nc=00000001,cnonce="c36a271f",qop="auth"

nonce="7a86c864b7fadff5457f90ec803a9182",uri="action/getConfig?name=VideoColor", response="909a78946ae1cf2395f9a1fd8fbeb38d"

# Camera

Camera API allows application to configure and view MERX video product settings.

## 4.1 Stream

### 4.1.1 GetStream

| URL Syntax | rtsp://<ip>:<port>/<channelNo>/<typeNo> |
| --- | --- |
| Comment | <ip> :the IP address of the MERX video product. <port >:the default port is 554. It can be omitted. <channelNo> :the channel number. It starts from ch00. <typeNo> :the stream type. The <typeNo> of main stream is 0, sub stream is 1. For example, we request the extra stream 1 of channel 1, the URL is: rtsp://192.168.6.67:554/ch01/0. |

## 4.2 CameraCap

### 4.2.1 GetCameraConfig

| URL Syntax | http://<ip>/action/getConfig?name=Camera |
| --- | --- |
| Description | camera options contain Backlight, ExposureSpeed, DayNightColor, and so on. |
| Response | Camera.IRCutMode=0 Camera.IRCutDelay=3 Camera.IRCutSensitive=1 Camera.IRFuncType=0 Camera.Mirror=0 Camera.Flip=0 Camera.Rotate=0 Camera.BackLightMode=1 Camera.BackLightLevel=1 Camera.R3dnrMode=1 Camera.R3dnrThreshTarget=50 Camera.DISEnable=1 Camera.DefogMode=1 Camera.DefogStrength=128 Camera.DwdrMode=1 Camera.DwdrStrength=50 Camera.GainControlMode=2 Camera.WBMode=0 Camera.Rgain=50 Camera.Ggain=50 Camera.Bgain=50 Camera.ShutterMode=0 Camera.ShutterSpeed=25 Camera.FlickerCtrl=0 |
| Comment | ChannelNo = video channel index. Current default channel 0. |

### 4.2.2 SetCameraConfig

| URL Syntax | http://<ip>/action/setConfig?name=Camera&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | In below table, head =Camera[ChannelNo] ChannelNo = video channel index. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Camera.IRCutMode | char | Range is {0, 1, 2, 3} 0 – auto. 1 – day. 2- night. 3 – video auto |
| Camera.IRCutDelay | char | Range is [0 ~ 36]. unit : second |
| Camera.IRCutSensitive | char | Range is {0, 1, 2} 0: High. 1: Middle. 2: Low. |
| Camera.IRFuncType | char | Infrared function switch. 0: close, 1: auto. |
| Camera.Mirror | char | Range is {0, 1}. Flip Horizontal 0: close. 1: open. |
| Camera.Flip | char | Range is {0, 1}. Flip vertical 0: close. 1: open. |
| Camera.Rotate | char | Range is {0, 1, 2, 3} 0: does not rotate. 1: 90° clockwise. 2: 180° clockwise. 3: 270° clockwise. |
| Camera.BackLightMode | char | Range is {0, 1} 0: disable. 1: enable. |
| Camera.BackLightLevel | char | Range is {0,1,2} 0: low 1: middle 2: high |
| Camera.R3dnrMode | char | Range is {0, 1, 2} 0: disable. 1: auto. 2: manual |
| Camera.R3dnrThreshTarget | unsigned char | Range is [0 ~ 0xff] thresh value when manual. |
| Camera.DISEnable | char | Range is {0, 1} 0: disable. 1: enable. |
| Camera.DefogMode | char | Range is {0, 1, 2} 0 : disable. 1: auto. 2: manual. |
| Camera.DefogStrength | char | Range is [0 ~ 100] Defog strength when used in manual mode. |
| Camera.DwdrMode | char | Range is {0, 1} 0: disable. 1: enable. |
| Camera.DwdrStrength | unsigned char | Range is [0 ~ 0xff] Drdw value when enabled DrdwMode. |
| Camera.GainControlMode | char | Range is {0, 1, 2, 3} 0: off. 1: low. 2: middle. 3: high |
| Camera.WBMode | char | Range is {0, 1, 2} 0: auto. 1: manual. 2: indoor. |
| Camera.Rgain | unsigned char | Range is [0 ~ 0xff]. |
| Camera.Ggain | unsigned char | Range is [0 ~ 0xff]. |
| Camera.Bgain | unsigned char | Range is [0 ~ 0xff]. |
| Camera.ShutterMode | char | Range is {0, 1}. 0: auto. 1: manual. |
| Camera.ShutterSpeed | char | Range is [0 ~ 30] ShutterUsecs value when manual. Max 1/25 in 50HZ, or max 1/30 in 60HZ. |
| Camera.FlickerCtrl | char | Range is {0, 1, 2}. 0: 50HZ. 1: 60HZ. 2: disable. |

## 4.3 VideoColor

### 4.3.1 GetVideoColorConfig

| URL Syntax | http://<ip>/action/getConfig?name=VideoColor |
| --- | --- |
| Response | Color.Brightness=50 Color.Contrast=50 Color.Hue=50 Color.Saturation=50 Color.Sharpness=50 |
| Comment | ChannelNo = video channel index. Current default channel 0. |

### 4.3.2 SetVideoColorConfig

| URL Syntax | http://<ip>/action/setConfig?name=VideoColor&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Response | OK or ERROR |
| Comment | ChannelNo = video channel index. Current default channel 0. |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Color.Brightness | unsigned char | Brightness, range is [0 ~ 255] |
| Color.Contrast | unsigned char | Contrast, range is [0 ~ 255] |
| Color.Hue | unsigned char | Hue, range is [0 ~ 255] |
| Color.Saturation | unsigned char | Saturation, range is [0 ~ 255] |
| Color.Sharpness | unsigned char | Sharpness, range is [0 ~ 255] |

### 4.3.3 Resolution

| Fixed Resolution Name | Size in PAL | Size in NTSC |
| --- | --- | --- |
| "D1" | 704 x 576 | 704 x 480 |
| "HD1" | 352 x 576 | 352 x 480 |
| "BCIF" | 704 x 288 | 704 x 240 |
| "CIF" | 352 x 288 | 352 x 240 |
| "QCIF" | 176 x 144 | 176 x 120 |
| "VGA" | 640 x 480 |
| "QVGA" | 320 x 240 |
| "SVCD" | 480 x 480 |
| "QQVGA" | 160 x 128 |
| "SVGA" | 800 x 592 |
| "XVGA" | 1024 x 768 |
| "WXGA" | 1280 x 800 |
| "SXGA" | 1280 x 1024 |
| "WSXGA" | 1600 x 1024 |
| "UXGA" | 1600 x 1200 |
| "WUXGA" | 1920 x 1200 |
| "ND1" | 240 x 192 |
| "720" | 1280 x 720 |
| "1080" | 1920 x 1080 |
| "1280x960" | 1280 x 960 (1.3 Mega Pixels) |
| "1872x1408" | 1872 x 1408 (2.5 Mega Pixels) |
| "3744x1408" | 3744 x 1408 (5 Mega Pixels) |
| "2048x1536" | 2048 x 1536 (3 Mega Pixels) |
| "2432x2048" | 2432 x 2048 (5 Mega Pixels) |
| "1216x1024" | 1216 x 1024 (1.2 Mega Pixels) |
| "1408x1024" | 1408 x 1024 (1.5 Mega Pixels) |
| "3296x2472" | 3296 x 2472 (8 Mega Pixels) |
| "2560x1920" | 2560 x 1920 (5 Mega Pixels) |
| "960H", | 960 x 576 | 960 x 480 |
| "DV720P" | 960 x 720 |

# 5. Live

## 5.1 Live General

### 5.1.1 GetLiveGeneralConfig

| URL Syntax | http://<ip>/action/getConfig?name=Live |
| --- | --- |
| Comment | Get the general live config . Current not support. |
| Response | Live.ActionSwitch=1 Live.StreamChoice=0 |

### 5.1.2 SetLiveGeneralConfig

| URL Syntax | http://<ip>/action/setConfig?name=Live&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Set the general live config. Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Live.ActionSwitch | char | Show record or alarm flag in preview window. |
| Live.StreamChoice | char | Preview stream. Range is {0, 1}. 0: main stream. 1: sub stream |

## 5.2 OSD

### 5.2.1 GetOSDConfig

| URL Syntax | http://<ip>/action/getConfig?name=OSD |
| --- | --- |
| Comment | OsdNo : index of OSD. 0 = osd 1 1 = osd 2 2 = osd 3 3 = osd 4 |
| Response | Osd[OsdNo].OSDSwitch=1 Osd[OsdNo].OSDType=0 Osd[OsdNo].Alpha=50 Osd[OsdNo].Content=MERX-ipc Osd[OsdNo].PosX=20 Osd[OsdNo].PosY=20 |

### 5.2.2 SetOSDConfig

| URL Syntax | http://<ip>/action/setConfig?name=OSD&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | OsdNo : index of OSD. 0 = osd 1 1 = osd 2 2 = osd 3 3 = osd 4 |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Osd[OsdNo].OSDSwitch | char | Osd switch. 0: disable ; 1: enable. |
| Osd[OsdNo].OSDType | char | Osd type. 0: time; 1: channel. |
| Osd[OsdNo].Alpha | unsigned char | Transparency of overlaid osd, the smaller the value, the more transparent it will be. Range is [0 ~ 128]. |
| Osd[OsdNo].Content | string | Content of overlaid osd. Max length: 64. |
| Osd[OsdNo].PosX | integer | Osd postion. Top left x coordinate. |
| Osd[OsdNo].PosY | integer | Osd postion. Top left y coordinate. |

## 5.3 VideoCover

### 5.3.1 GetVideoCoverConfig

| URL Syntax | http://<ip>/action/getConfig?name=VideoCover |
| --- | --- |
| Description | Video cover config. |
| Response | Cover.Switch=1 Cover[CoReg ].Enable=1 Cover[CoReg ].Rect.X=10 Cover[CoReg ].Rect.Y=30 Cover[CoReg ].Rect.Width=100 Cover[CoReg ].Rect.Height=100 |
| Comment | CoReg : Cover Region. Covers is an array which sustains multi- Cover regions 0 = region 1 1 = region 2 2 = region 3 3 = region 4 head=Cover[CoReg] |

### 5.3.2 SetVideoCoverConfig

| URL Syntax | http://<ip>/action/setConfig?name=VideoCover&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | CoReg : Cover region index Covers is an array which contains multiple cover regions 0 = region 1 1 = region 2 2 = region 3 3 = region 4 head = Cover[CoReg] |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Cover.Switch | char | Video cover switch. 0: disable; 1: enable. |
| Cover[CoReg ].Enable | char | Each cover area switch. 0: disable; 1: enable. |
| Cover[CoReg ].Rect.X | integer | top left corner x coordinate (left) |
| Cover[CoReg ].Rect.Y | integer | top left corner y coordinate (top) |
| Cover[CoReg ].Rect.Width | integer | rect width. Range is [0 ~ 65535]. |
| Cover[CoReg ].Rect.Height | integer | rect height. Range is [0 ~ 65535]. |

## 5.4 ROI

### 5.4.1 GetROIConfig

| URL Syntax | http://<ip>/action/getConfig?name=ROI&type=<StreamType> |
| --- | --- |
| Description | Stream ROI config. |
| Response | ROI[RoiNo].Index=5 ROI[RoiNo].Switch=1 ROI[RoiNo].IsAbsQp=1 ROI[RoiNo].Level=6 ROI[RoiNo].BgFrameRate=30 ROI[RoiNo].Rect.X=10 ROI[RoiNo].Rect.Y=30 ROI[RoiNo].Rect.Width=100 ROI[RoiNo].Rect.Height=100 |
| Comment | RoiNo : ROI index. Valid value range is [0 ~ 7]. head=ROI[RoiNo ] StreamType : 0 -- mainstream; 1 -- substream; 2 -- mobilestream. |

### 5.4.2 SetROIConfig

| URL Syntax | http://<ip>/action/setConfig?name=ROI&type=<StreamType>&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | RoiNo : ROI index. Valid value range is [0 ~ 7]. head=ROI[RoiNo ] StreamType : 0 -- mainstream; 1 -- substream; 2 -- mobilestream. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| ROI[RoiNo].Index | char | Range is [0 ~ 7]. Roi index, same as priority. The larger the index, the higher the priority. |
| ROI[RoiNo].Switch | char | 0: disable. 1: enable. |
| ROI[RoiNo].IsAbsQp | char | Range is {0, 1}. Whether to use absolute image quality. 0: relative quality. 1: absolute quality. |
| ROI[RoiNo].ILevel | char | Range is [1 ~ 6]. Roi value. The larger the value, the better the image quality. |
| ROI[RoiNo].BgFrameRate | char | Range is [0 ~ 30] Frame rate of non-ROI region. |
| ROI[RoiNo].Rect.X | integer | Range is [0 ~ 65535]. top left corner x coordinate (left). |
| ROI[RoiNo].Rect.Y | integer | Range is [0 ~ 65535]. top left corner y coordinate (top). |
| ROI[RoiNo].Rect.Width | integer | rect width. |
| ROI[RoiNo].Rect.Height | integer | rect height. |

# 6. Stream

## 6.1 MainStream

### 6.1.1 GetMainStreamConfig

| URL Syntax | http://<ip>/action/getConfig?name=MainStream |
| --- | --- |
| Response | MainStream.VideoType=0 MainStream.BitrateType=0 MainStream.BitrateMode=0 MainStream.Fps=25 MainStream.CustomBitrate=4096 MainStream.Bitrate=3 MainStream.Resolution=1 MainStream.VideoQuality=4 MainStream.IFrameInterval=30 MainStream.LoadBalancing=0 MainStream.AudioSwitch=1 MainStream.ProfileLevel=1 |
| Comment | Channel: video channel index. Current default 0. |

### 6.1.2 SetMainStreamConfig

| URL Syntax | http://<ip>/action/setConfig?name=MainStream&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Channel: video channel index. Current default 0. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| MainStream.VideoType | char | Range is {0, 1}. Video rate type. 0: H.264. 1: H.265. |
| MainStream.BitrateType | char | Range is {0, 1, 2}. 0: CBR. 1: VBR. 2. FIX QP |
| MainStream.BitrateMode | char | Range is {0, 1}. Rate mode. 0: pre define. 1: self define. |
| MainStream.Fps | char | Range is [1 ~ 25 ]. PAL; or [1 ~ 30] NTSC. Frames per second. |
| MainStream.CustomBitrate | unsigned integer | Range is [1 ~ 16M]. Bitrate value that user can choose. |
| MainStream.Resolution | char | Range {0, 1, 2, 3, 4, 5}. 0: 300W. 1: 1080P. 2: 960P. 3: 720P. 4: VGA. 5: QVGA. |
| MainStream.VideoQuality | char | Range {0, 1, 2, 3, 4, 5}. 0: worst. 1: worse. 2: pool. 3: good. 4: better. 5: best. |
| MainStream.IFrameInterval | char | Range is [1 ~ 100]. unit is second. I Frame interval. |
| MainStream.LoadBalancing | char | Range is {0, 1}. Load balance. 0: real time 1: balanced. |
| MainStream.AudioSwitch | char | Audio switch. 0: off. 1: on. |
| ProfileLevel | char | Range is {0, 1, 2}. Profile level. 0: Baseline. 1: Main Profile. 2: High Profile. |

## 6.2 Sub Stream

### 6.2.1 GetSubStreamConfig

| URL Syntax | http://<ip>/action/getConfig?name=SubStream |
| --- | --- |
| Response | SubStream.VideoType=0 SubStream.BitrateType=0 SubStream.BitrateMode=0 SubStream.Fps=15 SubStream.CustomBitrate=2048 SubStream.Bitrate=3 SubStream.Resolution=1 SubStream.VideoQuality=4 SubStream.IFrameInterval=30 SubStream.LoadBalancing=0 SubStream.AudioSwitch=1 ProfileLevel=1 |
| Comment | Channel: video channel index. Current default 0. |

### 6.2.2 SetSubStreamConfig

| URL Syntax | http://<ip>/action/setConfig?name=SubStream&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Channel: video channel index. Current default 0. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| SubStream.VideoType | char | Range is {0, 1}. Video rate type. 0: H.264. 1: H.265. |
| SubStream.BitrateType | char | Range is {0, 1, 2}. 0: CBR. 1: VBR. 2. FIX QP |
| SubStream.BitrateMode | char | Range is {0, 1}. Rate mode. 0: pre define. 1: self define. |
| SubStream.Fps | char | Range is [1 ~ 25 ]. PAL; or [1 ~ 30] . NTSC. Frames per second. |
| SubStream.CustomBitrate | unsigned integer | Range is [1 ~ 16M]. Bitrate value that user can choose. |
| SubStream.Resolution | char | Range {0, 1, 2, 3, 4, 5}. 0: 300W. 1: 1080P. 2: 960P. 3: 720P. 4: VGA. 5: QVGA. |
| SubStream.VideoQuality | char | Range {0, 1, 2, 3, 4, 5}. 0: worst. 1: worse. 2: pool. 3: good. 4: better. 5: best. |
| SubStream.IFrameInterval | char | Range is [1 ~ 100]. unit is second. I Frame interval. |
| SubStream.LoadBalancing | char | Range is {0, 1}. Load balance. 0: real time 1: balanced. |
| SubStream.AudioSwitch | char | Audio switch. 0: off. 1: on. |
| SubStream.ProfileLevel | char | Range is {0, 1, 2}. Profile level. 0: Baseline. 1: Main Profile. 2: High Profile. |

## 6.3 Mobile Stream

### 6.3.1 GetMobileStreamConfig

| URL Syntax | http://<ip>/action/getConfig?name=MobileStream |
| --- | --- |
| Response | MobileStream.VideoSwitch=1 MobileStream.VideoType=0 MobileStream.BitrateType=0 MobileStream.BitrateMode=0 MobileStream.Fps=10 MobileStream.CustomBitrate=512 MobileStream.Bitrate=5 MobileStream.Resolution=1 MobileStream.VideoQuality=4 MobileStream.IFrameInterval=30 MobileStream.LoadBalancing=0 MobileStream.AudioSwitch=1 MobileStream.ProfileLevel=1 |
| Comment | Channel: video channel index. Current default 0. |

### 6.3.2 SetMobileStreamConfig

| URL Syntax | http://<ip>/action/setConfig?name=MobileStream&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Channel: video channel index. Current default 0. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| MobileStream.VideoSwitch | char | Video switch. 0: disabled. 1: enabled. |
| MobileStream.VideoType | char | Range is {0, 1}. Video rate type. 0: H.264. 1: H.265. |
| MobileStream.BitrateType | char | Range is {0, 1, 2}. 0: CBR. 1: VBR. 2. FIX QP |
| MobileStream.BitrateMode | char | Range is {0, 1}. Rate mode. 0: pre define. 1: self define. |
| MobileStream.Fps | char | Range is [1 ~ 25 ]. PAL; or [1 ~ 30] . NTSC. Frames per second. |
| MobileStream.CustomBitrate | unsigned integer | Range is [1 ~ 16M]. Bitrate value that user can choose. |
| MobileStream.Resolution | char | Range {0, 1, 2, 3, 4, 5}. 0: 300W. 1: 1080P. 2: 960P. 3: 720P. 4: VGA. 5: QVGA. |
| MobileStream.VideoQuality | char | Range {0, 1, 2, 3, 4, 5}. 0: worst. 1: worse. 2: pool. 3: good. 4: better. 5: best. |
| MobileStream.IFrameInterval | char | Range is [1 ~ 100]. unit is second. I Frame interval. |
| MobileStream.LoadBalancing | char | Range is {0, 1}. Load balance. 0: real time 1: balanced. |
| MobileStream.AudioSwitch | char | Audio switch. 0: off. 1: on. |
| MobileStream.ProfileLevel | char | Range is {0, 1, 2}. Profile level. 0: Baseline. 1: Main Profile. 2: High Profile. |

## 6.4 Audio

### 6.4.1 GetAudioConfig

| URL Syntax | http://<ip>/action/getSysConfig?name=Audio |
| --- | --- |
| Response | Audio.Switch=1 Audio.Type=0 Audio.Bitrate=0 Audio.MicInVolume=5 Audio.LineOutVolume=6 |
| Comment | Channel: video channel index. Current default 0. |

### 6.4.2 SetAudioConfig

| URL Syntax | http://<ip>/action/setSysConfig?name=Audio&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Channel: video channel index. Current default 0. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Audio.Switch | unsigned char | Audio switch. 0: off. 1: on. |
| Audio.Type | char | Range is {0, 1, 2, 3}. Audio type. 0: G711A; 1: G711U. 2: G726; 3: ADPCM. |
| Audio.Bitrate | unsigned char | Current set to 0 which means 64k. |
| Audio.MicInVolume | unsigned char | Range is [0 ~ 10]. In volume value. |
| Audio.LineOutVolume | unsigned char | Range is [0 ~ 10]. Out volume value. |

# 7. NetWork

## 7.1 BasicConfig

### 7.1.1 GetBasicConfig

| URL Syntax | http://<ip>/action/getNetConfig?name=NetBase |
| --- | --- |
| Comment | Basic config contains basic network parameters (Default interface, domain name, host name), and configuration of each network interface. |
| Response | NetBase.IPAddress=192.168.1.240 NetBase.Netmask=255.255.255.0 NetBase.Gateway=192.168.1.1 NetBase.Dns1=8.8.8.8 NetBase.Dns2=221.96.128.86 NetBase.PPPOEuser=MERX NetBase.Password=519070 NetBase.NetworkMode=2 NetBase.ClientPort=9001 NetBase.WebPort=80 NetBase.MobilePort=18040 NetBase.UseUPNP=0 |

### 7.1.2 SetBasicConfig

| URL Syntax | http://<ip>/action/setNetConfig?name=NetBase&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| NetBase.IPAddress | string | Interface IP address. Max length: 32. |
| NetBase.Netmask | string | Network mask string: In the form of x.x.x.x, range of x is [0-255] Example: 255.255.255.0 |
| NetBase.Gateway | string | Gateway address. |
| NetBase.Dns1 | string | IP address of first DNS server. |
| NetBase.Dns2 | string | IP address of second DNS server. |
| NetBase.PPPOEuser | string | PPPoE User name. Max length: 32. |
| NetBase.Password | string | PPPoE User password. Max length: 32. |
| NetBase.NetworkMode | char | Range is {0, 1, 2}. Networking mode. 0: DHCP. 1: PPPOE. 2: manual. |
| NetBase.ClientPort | unsigned short | Client port. |
| NetBase.WebPort | unsigned short | Web port. |
| NetBase.MobilePort | unsigned short | Mobile port. |
| NetBase.UseUPNP | char | Enable / disable UPnP. 0: disable. 1: enable. |

## 7.2 3G

### 7.2.1 Get3GConfig

| URL Syntax | http://<ip>/action/getNetConfig?name=Net3G |
| --- | --- |
| Comment | Current not support. |
| Response | Net3G.Apn=ChinaNet Net3G.DataServer=123456 Net3G.UserName=MERX Net3G.Password=519070 Net3G.NetworkType=WCDMA |

### 7.2.2 Set3GConfig

| URL Syntax | http://<ip>/action/setNetConfig?name=Net3G&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Net3G.Apn | string | Data service access point. Max length: 24. |
| Net3G.DataServer | string | Data center number. Max length: 24. |
| Net3G.UserName | string | user name. Max length: 16. |
| Net3G.Password | string | User password. Max length: 16. |
| Net3G.NetworkType | char | Range is {1, 2, 3}. 1: WCDMA. 2: EVD0 3: ... |

## 7.3 Wifi

### 7.3.1 GetWifiConfig

| URL Syntax | http://<ip>/action/getNetConfig?name=Wifi |
| --- | --- |
| Comment | Current not support. |
| Response | Wifi.SSID=MERX Wifi.Password=519070 Wifi.IPAddress=192.168.1.114 Wifi.Gateway=192.168.1.1 Wifi.Netmask=255.255.255.0 Wifi.DNS=202.96.128.86 Wifi.EncryptType=WPA-PSK Wifi.AuthMode=AES Wifi.Switch=1 |

### 7.3.2 SetWifiConfig

| URL Syntax | http://<ip>/action/setNetConfig?name=Wifi&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Wifi.SSID | string | wifi hotspot. Max length: 32. |
| Wifi.Password | string | Wifi password. Max length: 32. |
| Wifi.IPAddress | string | IP address. Max length: 32. |
| Wifi.Gateway | string | Gateway of wifi. |
| Wifi.Netmask | string | Subnet mask. |
| Wifi.DNS | string | Domain server. |
| Wifi.EncryptType | char | Range is {0, 1, 2, 3, 4}. 0: NONE. 1: WEP. 2: WPA-PSK. 3: WPA2-PSK. 4: WPA-NONE. |
| Wifi.AuthMode | char | Range is {1, 2, 3, 4}. Authentication Mode. 1: OPEN. 2: SHARED. 3: TKIP. 4: AES. |
| Wifi.Switch | char | 0: close. 1: open. |

## 7.4 SSID

### 7.4.1 GetSSIDConfig

| URL Syntax | http://<ip>/action/getNetConfig?name=SSID |
| --- | --- |
| Comment | SSIDNo : index of recorded wifi hotspot. Valid value range is [0 ~ 4]. Current not support. |
| Response | SSID[SSIDNo ].SSID=MERX-free SSID[SSIDNo ].Protocol=802.11 SSID[SSIDNo ].EncryptType=WPA-PSK SSID[SSIDNo ].AuthMode=AES SSID[SSIDNo ].SignalQuality=5 SSID[SSIDNo ].Frequency=50 SSID[SSIDNo ].MacAddr=00:23:5c:f2:1c:b4 |

### 7.4.2 SetSSIDConfig

| URL Syntax | http://<ip>/action/setNetConfig?name=SSID&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | SSIDNo : index of recorded wifi hotspot. Valid value range is [0 ~ 4]. Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| SSID[SSIDNo ].SSID | string | Once connected wifi hotspot. Max length: 32. |
| SSID[SSIDNo ].Protocol | string | 802.11. Max length: 16. |
| SSID[SSIDNo ].EncryptType | char | Range is {0, 1, 2, 3, 4}. 0: NONE. 1: WEP. 2: WPA-PSK. 3: WPA2-PSK. 4: WPA-NONE. |
| SSID[SSIDNo ].AuthMode | char | Range is {1, 2, 3, 4}. Authentication Mode. 1: OPEN. 2: SHARED. 3: TKIP. 4: AES. |
| SSID[SSIDNo ].SignalQuality | char | Range is [0 ~ 5]. 0: lowest quality. 5: highest quality. |
| SSID[SSIDNo ].Frequency | unsigned char | Range is [1 ~ 255] |
| SSID[SSIDNo ].MacAddr | string | MAC address of wifi ssid. Max length: 6. |

## 7.5 DDNS

### 7.5.1 GetDDNSConfig

| URL Syntax | http://<ip>/action/getNetConfig?name=DDNS |
| --- | --- |
| Comment |  |
| Response | DDNS.HostName=MERX DDNS.ServerAddr=anlian.co DDNS.UserName=MERX DDNS.Password=519070 DDNS.UseFlag=1 DDNS.Switch=1 DDNS.UpdateInterval=3 |

### 7.5.2 SetDDNSConfig

| URL Syntax | http://<ip>/action/setNetConfig?name=DDNS&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| DDNS.HostName | string | Host name of this device. Max length: 32. |
| DDNS.ServerAddr | string | DDNS server IP address or name. Max length: 32. |
| DDNS.UserName | string | DDNS user name. Max length: 32. |
| DDNS.Password | string | DDNS user password. Max length: 32. |
| DDNS.UseFlag | unsigned integer | DDNS use flag. Each bit correspond to a type of DDNS. |
| DDNS.Switch | unsigned char | DDSN switch. 0: disable. 1: enable. |
| DDNS.UpdateInterval | unsigned char | Range is [0 ~ 255]. DDNS update interval. |

## 7.6 Email

### 7.6.1 GetEmailConfig

| URL Syntax | http://<ip>/action/getNetConfig?name=Email |
| --- | --- |
| Comment |  |
| Response | Email.Address=www.163.com Email.Sender=www.MERX.cn Email.Password=123456 Email.Receivers[0]=x@MERX.cn Email.Receivers[1]=y@MERX.cn Email.Receivers[2]=z@MERX.cn Email.Port=26 Email.SSLSwitch=1 Email.Switch=1 Email.Intervaltime=180 |

### 7.6.2 SetEmailConfig

| URL Syntax | http://<ip>/action/setNetConfig?name=Email&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Email.Address | string | SMTP server IP address or name. Max length: 32. |
| Email.Sender | string | Sender address. Max length: 32. |
| Email.Password | string | Sender password. Max length: 32. |
| Email.Receivers[0] | string | Email addresses of 3 receivers. Max length: 32. |
| Email.Receivers[1] |  |  |
| Email.Receivers[2] |  |  |
| Email.Port | unsigned short | Range is [1-65535]. |
| Email.SSLSwitch | char | 1: enable SSL email. |
| Email.EmailSwitch | char | 0: disable. 1: enable email. |
| Email.Intervaltime | short | Range is {180, 300, 600}. unit is second. |

## 7.7 P2P

### 7.7.1 GetP2PConfig

| URL Syntax | http://<ip>/action/getNetConfig?name=P2P |
| --- | --- |
| Comment |  |
| Response | P2P.Uid=rs123456 P2P.UserName=MERX P2P.Password=519070 P2P.State=1 |

### 7.7.2 SetP2PConfig

| URL Syntax | http://<ip>/action/setNetConfig?name=P2P&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| P2P.Uid | string | P2P id. Max length: 32. |
| P2P.UserName | string | P2P user name. Max length: 32. |
| P2P.Password | string | P2P user password. Max length: 32. |
| P2P.State | char | P2P connect status. |

## 7.8 RTSP

### 7.8.1 GetRTSPConfig

| URL Syntax | http://<ip>/action/getNetConfig?name=RTSP |
| --- | --- |
| Comment |  |
| Response | RTSP.UserName=MERX RTSP.Password=519070 RTSP.Port=554 RTSP.CheckFlag=1 RTSP.Switch=1 RTSP.AuthType=1 |

### 7.8.2 SetRTSPConfig

| URL Syntax | http://<ip>/action=setNetConfig?name=RTSP&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| RTSP.UserName | string | RTSP user name. Max length: 32. |
| RTSP.Password | string | RTSP user password. Max length: 32. |
| RTSP.Port | integer | Range is [1-65535]. Port of RTSP server. |
| RTSP.CheckFlag | char | 0: disable. 1: enable |
| RTSP.Switch | char | 0: disable. 1: enable. |
| RTSP.AuthType | char | Range is {0, 1, 2}. 0: none. 1: basic. 2. digest. |

## 7.9 FTP

### 7.9.1 GetFTPConfig

| URL Syntax | http://<ip>/action/getNetConfig?name=FTP |
| --- | --- |
| Comment | Return FTP server config. |
| Response | FTP.IPAddress=192.168.1.120 FTP.UserName=anonymity FTP.Password=123456 FTP.Port =21 FTP.Switch=1 FTP.TimeInterval = 3 FTP.ReqTypeMask =2 FTP.RecType =1 FTP.FilePath=share |

### 7.9.2 SetFTPConfig

| URL Syntax | http://<ip>/action/setNetConfig?name=FTP&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| FTP.IPAddress | string | FTP IP address. Max length: 32. |
| FTP.UserName | string | Login user name. Max length: 32. |
| FTP.Password | string | Login user password. Max length: 32. |
| FTP.Port | integer | FTP port. |
| FTP.Switch | char | 0: off. 1: on. |
| FTP.TimeInterval | char | Range is [0 ~ 128]. Period of time to upload video. |
| FTP.ReqTypeMask | char | Req type mask .Bitwise representation. 0 bit: close. 2bit: image. 3bit: video |
| FTP.RecType | char | Range is {1, 2, 3}. 1: normal record. 2: alarm record. 3: all record. |
| FTP.FilePath | string | FTP file path. Max length: 96. Directory name. |

## 7.10 Platform

### 7.10.1 GetPlatformConfig

| URL Syntax | http://<ip>/action/getNetConfig?name=Platform |
| --- | --- |
| Comment | Current not support. |
| Response | Platform.PuID=rs123456puid Platform.IPAddress=192.168.1.245 Platform.ShowTag=1 Platform.Port=3456 Platform.Select=1 Platform.Switch=1 Platform.MediaConType=0 |

### 7.10.2 SetPlatformConfig

| URL Syntax | http://<ip>/action/setNetConfig?name=Platform&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Platform.PuID | string | Platform PUID. Max length: 32. |
| Platform.IPAddress | string | Platform IP address. Max length: 32. |
| Platform.ShowTag | integer | Show tag. |
| Platform.Port | unsigned short | Platform port. |
| Platform.Select | char | Platform select. |
| Platform.Switch | char | 0: disable. 1: enable. |
| Platform.MediaConType | char | Server transfer protocol. 0: TCP. 1: UDP. |

## 7.11 Mobile

### 7.11.1 GetMobileConfig

| URL Syntax | http://<ip>/action/getNetConfig?name=Mobile |
| --- | --- |
| Comment | Current not support. |
| Response | Mobile.UserName=MERX Mobile.Password=519070 Mobile.IPAddress=192.168.1.10 Mobile.NetType=3G |

### 7.11.2 SetMobileConfig

| URL Syntax | http://<ip>/action/setNetConfig?name=Mobile&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Mobile.UserName | string | Mobile user name. Max length: 32. |
| Mobile.Password | string | Mobile user password. Max length: 32. |
| Mobile.IPAddress | string | Mobile IP Address. Max length: 32. |
| Mobile.NetType | char | Networking type. 0: 2.5G. 1: 2.75G. 2: 3G. 3: Wifi. |

## 7.12 GB28181

### 7.12.1 GetGB28181Config

| URL Syntax | http://<ip>/action/getNetConfig?name=GB28181 |
| --- | --- |
| Comment | Current not support. |
| Response | GB28181.DeviceId=3556 GB28181.AlarmId=123 GB28181.SipServerId=37777 GB28181.SipServerIP=192.168.1.129 GB28181.SipServerPwd=519070 GB28181.SipServerPort=5566 GB28181.Switch=1 |

### 7.12.2 SetGB28181Config

| URL Syntax | http://<ip>/action=setNetConfig?name=GB28181&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| GB28181.DeviceId | string | Device ID. Max length: 64. |
| GB28181.AlarmId | string | Alarm ID. Max length: 64. |
| GB28181.SipServerId | string | SIP Server ID. Max length: 32. |
| GB28181.SipServerIP | string | SIP Server IP. Max length: 32. |
| GB28181.SipServerPwd | string | SIP Server password. Max length: 64. |
| GB28181.SipServerPort | unsigned short | SIP Server port. |
| GB28181.Switch | char | 0: disable. 1: enable. |

# 8. Alarm

## 8.1 IO Alarm

### 8.1.1 GetIOAlarmConfig

| URL Syntax | http://<ip>/action/getAlarmConfig?name=IOAlarm |
| --- | --- |
| Comment |  |
| Response | IOAlarm.AlarmSet=1 IOAlarm.AlarmOutTime=10 IOAlarm.RecordDelayTime=30 IOAlarm.AlarmOutManager=1 IOAlarm.EmailLink=0 IOAlarm.RecordSwitch=1 IOAlarm.FtpUploadSwitch=0 IOAlarm.CloudSwitch=0 IOAlarm.PushSwitch=0 |

### 8.1.2 SetIOAlarmConfig

| URL Syntax | http://<ip>/action/setAlarmConfig?name=IOAlarm&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| IOAlarm.AlarmSet | char | Range is {0, 1, 2}. IO status alarm. 0: normal open. 1: normal close. 2: closed. |
| IOAlarm.AlarmOutTime | char | Range is 10, 20, 40, 60, 30s, 1min , 2min. |
| IOAlarm.RecordDelayTime | char | Range is 10, 30, 1min, 2min, 5mins. |
| IOAlarm.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| IOAlarm.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| IOAlarm.RecordSwitch | char | 0: disable. 1: enable. |
| IOAlarm.FtpUploadSwitch | char | 0: disable. 1: enable. |
| IOAlarm.CloudSwitch | char | 0: disable. 1: enable. |
| IOAlarm.PushSwitch | char | 0: disable. 1: enable. |

## 8.2 MotionDetect

### 8.2.1 GetMotionDetectConfig

| URL Syntax | http://<ip>/action/getAlarmConfig?name=Motion |
| --- | --- |
| Comment | MotionDetect config of a video channel contains Enable, Level, Region and so on. |
| Response | Motion.Switch=1 Motion.Sensitivity=4 Motion.AlarmOutTime=10 Motion.RecordDelayTime=30 Motion.AlarmOutManager=1 Motion.EmailLink=0 Motion.RecordSwitch=1 Motion.FtpUploadSwitch=0 Motion.CloudSwitch=0 Motion.PushSwitch=0 Motion.Region[0]=03-CD-5E-7F-12-6A-49-FB-6C-10-2D ... ... Motion.Region[17]=4B-AF-71-CE-38-90-A6-CA-DF-33-5C |

### 8.2.2 SetMotionDetectConfig

| URL Syntax | http://<ip>/action/setAlarmConfig?name=Motion&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Channel: video channel index LineNum Index of region, region is divided into lines and each line has several blocks, a line is divided into 44 bit , a bit for a block.. 0=Line 1 1=Line 2 … … 17= Line 18 |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Motion.Switch | char | Enable/Disable motion detect feature in a channel. |
| Motion.Sensitivity | char | Range is [1-8]. Sensitivity of motion detection. 1: lowest sensitivity. 8: highest sensitivity. |
| Motion.Region[LineNum] | integer | Currently, region is divided into 36 lines and 44 blocks/line. A bit describes a block in the line. Bit = 1: motion in this block is monitored.. Example: Region[0] = (FF-FF-FF-FF-FF-F0-00-00-00-00-00):: motion in channel 0 line 0’s 44 blocks is monitored. Line 1’s 44 blocks not monitored. |
| Motion.AlarmOutTime | char | Range is 10, 20, 40, 60, 30s, 1min , 2min. |
| Motion.RecordDelayTime | char | Range is 10, 30, 1min, 2min, 5mins. |
| Motion.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| Motion.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| Motion.RecordSwitch | char | 0: disable. 1: enable. |
| Motion.FtpUploadSwitch | char | 0: disable. 1: enable. |
| Motion.CloudSwitch | char | 0: disable. 1: enable. |
| Motion.PushSwitch | char | 0: disable. 1: enable. |

## 8.3 PerimeterLine

### 8.3.1 GetPerimeterLineConfig

| URL Syntax | http://<ip>/action/getAlarmConfig?name=PerimLine |
| --- | --- |
| Comment | LineNo below is the perimeter line index. Valid value range is [0 ~ 31]. |
| Response | PerimLine.ChnSwitch=1 PerimLine.AlarmOutTime=10 PerimLine.RecordDelayTime=30 PerimLine.AlarmOutManager=1 PerimLine.EmailLink=0 PerimLine.RecordSwitch=1 PerimLine.FtpUploadSwitch=0 PerimLine.CloudSwitch=0 PerimLine.PushSwitch=0 PerimLine.RuleSwitch=1 PerimLine.RuleType=1 PerimLine.LineTwoWay=1 PerimLine.Scene=1 PerimLine.Sensitive=3 PerimLine.RuleLine[LineNo ].StartX=10 PerimLine.RuleLine[LineNo ].StartY=10 PerimLine.RuleLine[LineNo ].EndX=20 PerimLine.RuleLine[LineNo ].EndY=30 |

### 8.3.2 SetPerimeterLineConfig

| URL Syntax | http://<ip>/action/setAlarmConfig?name=PerimLine&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | LineNo below is the perimeter line index. Valid value range is [0 ~ 31]. Each channel has at most 64 points coordinates. ie 32 lines. First line will be used if it’s satellite, if it’s perimeter, 8 lines will be connected together to form a closed figure. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| PerimLine.ChnSwitch | char | 0: close. 1: open. |
| PerimLine.AlarmOutTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. |
| PerimLine.RecordDelayTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. |
| PerimLine.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| PerimLine.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| PerimLine.RecordSwitch | char | 0: disable. 1: enable. |
| PerimLine.FtpUploadSwitch | char | 0: disable. 1: enable. |
| PerimLine.CloudSwitch | char | 0: disable. 1: enable. |
| PerimLine.PushSwitch | char | 0: disable. 1: enable. |
| PerimLine.RuleSwitch | char | Each channel use one byte to represent at most 4 rules. 0 - close; 1 - in use. |
| PerimLine.RuleType | char | Each channel use one byte to represent at most 4 rules type. 0 - satellite line; 1 - perimeter line. |
| PerimLine.LineTwoWay | char | Each channel use one byte to represent at most 4 satellite type. 0 - not two way; 1 - two way. |
| PerimLine.Scene | char | Scene. 0: indoor, 1: outdoor. |
| PerimLine.Sensitive | char | Sensitive. Range is {0, 1, 2, 3}. |
| PerimLine.RuleLine[LineNo ].StartX | short | Start x coordinate of perimeter line. |
| PerimLine.RuleLine[LineNo ].StartY | short | Start y coordinate of perimeter line. |
| PerimLine.RuleLine[LineNo ].EndX | short | End x coordinate of perimeter line. |
| PerimLine.RuleLine[LineNo ].EndY | short | End y coordinate of perimeter line. |

## 8.4 OSCAlarm

### 8.4.1 GetOSCAlarm

| URL Syntax | http://<ip>/action/getAlarmConfig?name=OSCAlarm |
| --- | --- |
| Comment | RectNo below is the OSC rect index. Valid value range is [0 ~ 15]. |
| Response | OSCAlarm.ChnSwitch=1 OSCAlarm.AlarmOutTime=10 OSCAlarm.RecordDelayTime=30 OSCAlarm.AlarmOutManager=1 OSCAlarm.EmailLink=0 OSCAlarm.RecordSwitch=1 OSCAlarm.FtpUploadSwitch=0 OSCAlarm.CloudSwitch=0 OSCAlarm.PushSwitch=0 OSCAlarm.RuleSwitch=1 OSCAlarm.RuleType=1 OSCAlarm.RuleRectEnable[0]=1 OSCAlarm.RuleRectEnable[1]=1 OSCAlarm.RuleRectEnable[2]=1 OSCAlarm.RuleRectEnable[3]=1 OSCAlarm.Scene=1 OSCAlarm.Sensitive=2 OSCAlarm.Rect[RectNo ].X=10 OSCAlarm.Rect[RectNo ].Y=10 OSCAlarm.Rect[RectNo ].Width=50 OSCAlarm.Rect[RectNo ].Height=50 |

### 8.4.2 SetOSCAlarm

| URL Syntax | http://<ip>/action/setAlarmConfig?name=OSCAlarm |
| --- | --- |
| Comment | RectNo below is the OSC rect index. Valid value range is [0 ~ 15]. Total regions is at most 16. 0 ~ 3 is used for the first rule; 4 ~ 7 is used for the second rule; 8 ~ 11 is used for the third rule; 12 ~ 15 is used for the forth rule. |
| Response | result=2 |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| OSCAlarm.ChnSwitch | char | 0: close. 1: open. |
| OSCAlarm.AlarmOutTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. |
| OSCAlarm.RecordDelayTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. |
| OSCAlarm.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| OSCAlarm.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| OSCAlarm.RecordSwitch | char | 0: disable. 1: enable. |
| OSCAlarm.FtpUploadSwitch | char | 0: disable. 1: enable. |
| OSCAlarm.CloudSwitch | char | 0: disable. 1: enable. |
| OSCAlarm.PushSwitch | char | 0: disable. 1: enable. |
| OSCAlarm.RuleSwitch | char | Each channel use one byte to represent at most 4 rules. 0 - close; 1 - in use. |
| OSCAlarm.RuleType | char | Each channel use one byte to represent at most 4 rules type. 0 - left; 1 - lost. |
| OSCAlarm.RuleRectEnable[0] | char | Each channel has at most 4 rules, each rule has at most 4 regions, each bit represent a status of a region. 0 - disable; 1 - enable. |
| OSCAlarm.RuleRectEnable[1] |  |  |
| OSCAlarm.RuleRectEnable[2] |  |  |
| OSCAlarm.RuleRectEnable[3] |  |  |
| OSCAlarm.Scene | char | Scene. 0: indoor, 1: outdoor. |
| OSCAlarm.Sensitive | char | Sensitive. Range is {0, 1, 2, 3}. |
| OSCAlarm.Rect[RectNo ].X | integer | Left coordinate of rule rect. |
| OSCAlarm.Rect[RectNo ].Y | integer | Top coordinate of rule rect. |
| OSCAlarm.Rect[RectNo ].Width | integer | Width of rule rect. |
| OSCAlarm.Rect[RectNo ].Height | integer | Height of rule rect. |

## 8.5 ODAlarm

### 8.5.1 GetODAlarm

| URL Syntax | http://<ip>/action/getAlarmConfig?name=ODAlarm |
| --- | --- |
| Comment |  |
| Response | ODAlarm.Switch=1 ODAlarm.Sensitivity=3 ODAlarm.AlarmOutTime=10 ODAlarm.RecordDelayTime=30 ODAlarm.AlarmOutManager=1 ODAlarm.EmailLink=0 ODAlarm.RecordSwitch=1 ODAlarm.FtpUploadSwitch=0 ODAlarm.CloudSwitch=0 ODAlarm.PushSwitch=0 |

### 8.5.2 SetODAlarm

| URL Syntax | http://<ip>/action/setAlarmConfig?name=ODAlarm |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| ODAlarm.Switch | char | 0: disable. 1: enable. |
| ODAlarm.Sensitivity | char | Range is [1 ~ 6]. Sensitivity of OD. 1: lowest sensitivity. 6: highest sensitivity. |
| ODAlarm.AlarmOutTime | char | Range is 10, 20, 40, 60, 30s, 1min , 2min. |
| ODAlarm.RecordDelayTime | char | Range is 10, 30, 1min, 2min, 5mins. |
| ODAlarm.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| ODAlarm.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| ODAlarm.RecordSwitch | char | 0: disable. 1: enable. |
| ODAlarm.FtpUploadSwitch | char | 0: disable. 1: enable. |
| ODAlarm.CloudSwitch | char | 0: disable. 1: enable. |
| ODAlarm.PushSwitch | char | 0: disable. 1: enable. |

# 9. Record & Snap

## 9.1 General Record

### 9.1.1 GetGeneralRecConfig

| URL Syntax | http://<ip>/action/getConfig?name=GeneralRec |
| --- | --- |
| Comment | Current not support. |
| Response | Record.ChnSwitch=1 Record.PreRecSwitch=1 Record.State=1 Record.Mode=1 Record.StreamMode=0 |

### 9.1.2 SetGeneralRecConfig

| URL Syntax | http://<ip>/action/setConfig?name=GeneralRec&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Record.ChnSwitch | char | 0: close. 1: open. |
| Record.PreRecSwitch | char | 0: close. 1: open. |
| Record.State | char | Record automatically restored when power off restart. |
| Record.Mode | char | 0: Timer recording. 1: Boot recording. |
| Record.StreamMode | char | 0: mainstream. 1: substream. |

## 9.2 Smart Record

### 9.2.1 GetSmartRecConfig

| URL Syntax | http://<ip>/action/getConfig?name=SmartRec |
| --- | --- |
| Comment | Current not support. |
| Response | SmartRec.Type=0 |

### 9.2.2 SetSmartRecConfig

| URL Syntax | http://<ip>/action=setConfig?name=SmartRec&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | channel in below table is video channel index, start form 0. Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| SmartRec.Type | char | Range is {0, 1}. 0: motion record 1: smart record |

## 9.3 Schedule

### 9.3.1 GetScheduleConfig

| URL Syntax | http://<ip>/action/getConfig?name=Schedule |
| --- | --- |
| Comment | Channel in below table is video channel number, weekday range is [0-6] (Sunday - Saturday). Time range is [0 ~ 1]. Half hour as a unit. |
| Response | Schedule[0][0]=FFFFFFFFFFFFFFFFFFFFFFFF Schedule[0][1]=FFFFFFFFFFFFFFFFFFFFFFFF Schedule[1][0]=FFFFFFFFFFFFFFFFFFFFFFFF Schedule[1][1]=FFFFFFFFFFFFFFFFFFFFFFFF ... Schedule[6][0]=000000000000000000000000 Schedule[6][1]=000000000000000000000000 |

### 9.3.2 SetScheduleConfig

| URL Syntax | http://<ip>/action=setConfig?name=Schedule&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | In below table: ch = channel index, wd = week day index, ts = time section index. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Schedule[wd][ts] | char | wd (week day) range is [0 ~ 6] (Sunday - Staurday) ts (time section) range is [0 ~ 1], timesection table index. Bit 1: normal record schedule. Bit 2: motion record schedule. Bit 3: IO alarm record schedule. Bit 4: intelligence record schedule. |

## 9.4 Snap

### 9.4.1 GetSnapConfig

| URL Syntax | http://<ip>/action/getConfig?name=Snap |
| --- | --- |
| Comment | Channel in below table is video channel number. Current not support. |
| Response | Snap.Switch=1 Snap.Type=2 Snap.Interval=20 Snap.Quality=1 |

### 9.4.2 SetSnapConfig

| URL Syntax | http://<ip>/action/setConfig?name=Snap&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Snap.Switch | char | 0: disable. 1: enable. |
| Snap.Type | char | Bitwise value. 0: motion. 1: IO. 2: smart. |
| Snap.Interval | char | Range is [1 ~ 100]. |
| Snap.Quality | char | Image quality of capture. |

# 10. System

## 10.1 General

### 10.1.1 GetSysGeneralConfig

| URL Syntax | http://<ip>/action/getSystemConfig?name=SystemInfo |
| --- | --- |
| Comment |  |
| Response | System.LangUseFlag=1 System.CurrentLang=1 System.VideoFormat=1 System.DateMode=0 System.TimeMode=0 System.Time=2015-06-18_15:03:00 System.MaintainSwitch=1 System.MaintainPeriod1=0 System.MaintainPeriod2=1 System.MaintainTime=03:00 |

### 10.1.2 SetSysGeneralConfig

| URL Syntax | http://<ip>/action/setSystemConfig?name=SystemInfo&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| System.LangUseFlag | integer | Language flag of current usage, one bit represent a kind of language. |
| System.CurrentLang | char | Current system language. |
| System.VideoFormat | char | 0 - TS_PAL, 1 - TS_NTSC |
| System.DateMode | char | Date mode |
| System.TimeMode | char | Time mode. 0: 24 hours mode. 1: 12 hours mode. |
| System.Time | string | System time . Format: Year-month-Day_Hour:minute:Second . |
| System.MaintainSwitch | char | 0: close. 1: open. |
| System.MaintainPeriod1 | char | 0: every day. 1: every week. 2: every month. |
| System.MaintainPeriod2 | char | Some day in a week or some day in a month. |
| System.MaintainTime | string | Maintain time . Format: Hour:minute . |

## 10.2 User

### 10.2.1 GetUserInfo

| URL Syntax | http://<ip>/action/getSystemConfig?name=UserInfo&index=<UserNo> |
| --- | --- |
| Comment | UserNo: user list index. Valid value range is [0 ~ 6]. 0 : admin |
| Response | User[UserNo].UserName=MERX User[UserNo].Password=519070 User[UserNo].PwdConfirm=519070 User[UserNo].SetRight=1 User[UserNo].PreviewChannel=1 User[UserNo].PlayBackChannel=1 User[UserNo].BackupChannel=1 User[UserNo].PlayBack=1 User[UserNo].Backup=1 User[UserNo].Preview=1 User[UserNo].Switch=1 User[UserNo].PwdSwitch=0 User[UserNo].IsLive=1 |

### 10.2.2 GetUserInfoAll

| URL Syntax | http://<ip>/action/getSystemConfig?name=UserInfoAll |
| --- | --- |
| Comment | UserNo: user list index. Valid value range is [0 ~ 6]. |
| Response | User[UserNo].UserName=MERX User[UserNo].Password=519070 User[UserNo].PwdConfirm=519070 User[UserNo].SetRight=1 User[UserNo].PreviewChannel=1 User[UserNo].PlayBackChannel=1 User[UserNo].BackupChannel=1 User[UserNo].PlayBack=1 User[UserNo].Backup=1 User[UserNo].Preview=1 User[UserNo].Switch=1 User[UserNo].PwdSwitch=0 User[UserNo].IsLive=1 |

### 10.2.3 SetUserConfig

| URL Syntax | http://<ip>/action/setSystemConfig?name=UserInfo |
| --- | --- |
| Comment | UserNo: user list index. Valid value range is [0 ~ 6]. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| User[UserNo].UserName | string | User name. Max length: 32. |
| User[UserNo].Password | string | User password. Max length: 32. |
| User[UserNo].PwdConfirm | string | User password conform. Max length: 32. |
| User[UserNo].SetRight | integer | Set right. Bitwise value. |
| User[UserNo].PreviewChannel | integer | Preview channel . |
| User[UserNo].PlayBackChannel | integer | Playback channel. |
| User[UserNo].BackupChannel | integer | Backup channel. |
| User[UserNo].PlayBack | char | Record playback right. |
| User[UserNo].Backup | char | Bakcup right |
| User[UserNo].Preview | char | Preview right. |
| User[UserNo].Switch | char | User in use. 0: not use. 1: in use. |
| User[UserNo].PwdSwitch | char | Login password switch. 0: close. 1: open. |
| User[UserNo].IsLive | char | User is on line. 0: off line. 1: on line. |

## 10.3 NTP

### 10.3.1 GetNTPConfig

| URL Syntax | http://<ip>/action/getSystemConfig?name=NTP |
| --- | --- |
| Comment |  |
| Response | NTP.Switch=1 NTP.Server=3 NTP.Port=12 NTP.SyncPeriod=31 NTP.TimeZone=8 |

### 10.3.2 SetNTPConfig

| URL Syntax | http://<ip>/action/setSystemConfig?name=NTP&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| NTP.Switch | char | Enable/Disable NTP server. |
| NTP.Server | char | NTP server flag. |
| NTP.Port | short | Range is [1-65535]. Port of NTP server. |
| NTP.SyncPeriod | short | Range is [0-65535], unit is minutes |
| NTP.TimeZone | char | Range is [0-32]. 0: "GMT+00:00" 1: "GMT+01:00" 2: "GMT+02:00" 3: "GMT+03:00" 4: "GMT+03:30" 5: "GMT+04:00" 6: "GMT+04:30" 7: "GMT+05:00" 8: "GMT+05:30" 9: "GMT+05:45" 10: "GMT+06:00" 11: "GMT+06:30" 12: "GMT+07:00" 13: "GMT+08:00" 14: "GMT+09:00" 15: "GMT+09:30" 16: "GMT+10:00" 17: "GMT+11:00" 18: "GMT+12:00" 19: "GMT+13:00" 20: "GMT-01:00" 21: "GMT-02:00" 22: "GMT-03:00" 23: "GMT-03:30" 24: "GMT-04:00" 25: "GMT-05:00" 26: "GMT-06:00" 27: "GMT-07:00" 28: "GMT-08:00" 29: "GMT-09:00" 30: "GMT-10:00" 31: "GMT-11:00" 32: "GMT-12:00" |

## 10.4 DST

### 10.4.1 GetDSTConfig

| URL Syntax | http://<ip>/action/getSystemConfig?name=DST |
| --- | --- |
| Comment |  |
| Response | DST.StartHour=00:00:00 DST.EndHour=23:59:59 DST.StartDate=2015-04-12 DST.EndDate=2015-04-12 DST.StartMonth=1 DST.EndMonth=2 DST.StartWeek=0 DST.EndWeek=1 DST.StartWeekDay=1 DST.EndWeekDay=2 DST.Switch=0 DST.Mode=0 DST.HaveDstTime=1 DST.Offset=0 |

### 10.4.2 SetDSTConfig

| URL Syntax | http://<ip>/action/setSystemConfig?name=DST&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| DST.StartHour | string | Dst start time. Format : hour:minute:second. |
| DST.EndHour | string | Dst end time. Format : hour:minute:second. |
| DST.StartDate | string | Dst start date. Format: year-month-day. |
| DST.EndDate | string | Dst end date. Format: year-month-day. |
| DST.StartMonth | char | Range is [0 ~ 11]. |

| DST.EndMonth | char | Range is [0 ~ 11]. |
| --- | --- | --- |
| DST.StartWeek | char | Range is {0, 1, 2, 3, 4}. 0: the first week, 1: the second week... |
| DSY.EndWeek | char | Range is {0, 1, 2, 3, 4}. 0: the first week, 1: the second week... |
| DST.StartWeekDay | char | Which day start from. 0-Sun, 1-Mon, ... 6-Sat |
| DST.EndWeekDay | char | Which day end of. 0-Sun, 1-Mon, ... 6-Sat |
| DST.Switch | char | Enable/Disable DST (daylight saving time) |
| DST.Mode | char | 0: Week. 1: Date. |
| DST.HaveDstTime | char | 0: not DST. 1: is DST. |
| DST.Offset |  | Dst offset value. 0: 1hour. 1: 2hour. |

# 11. Storage

## 11.1 CloudStorage

### 11.1.1 GetCloudStorageConfig

| URL Syntax | http://<ip>/action/getSystemConfig?name=CloudStorage |
| --- | --- |
| Comment | Currently only use one cloud user. Current not support. |
| Response | Cloud.Key[0]=MERX Cloud.Password[0]=123456 Cloud.Key[1]= Cloud.Password[1]= Cloud.Key[2]= Cloud.Password[2]= Cloud.DirName=cloud Cloud.FtpPath=ftp Cloud.Switch=1 Cloud.Type=0 Cloud.TimeTrigger=0 Cloud.Version=1.2.1 |

### 11.1.2 SetCloudStorageConfig

| URL Syntax | http://<ip>/action=setSystemConfig?name=CloudStorage&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Currently only use one cloud user. Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Cloud.Key[0] | string | User key. Max length: 128. |
| Cloud.Key[1] |  |  |
| Cloud.Key[2] |  |  |
| Cloud.Password[0] | string | User key password. Max length: 128. |
| Cloud.Password1] |  |  |
| Cloud.Password[2] |  |  |
| Cloud.DirName | string | Upload direction. Max length: 32. |
| Cloud.FtpPath | string | ftp upload path. Max length: 96. |
| Cloud.Switch | char | Enable/Disable the cloud. |
| Cloud.Type | char | 0-DROPBOX, 1-GOOGLE |
| Cloud.TimeTrigger | char | Trigger time |
| Cloud.Version | string | Cloud version. Max length: 8. |

## 11.2 Device Storage

### 11.2.1 GetDevStorageConfig

| URL Syntax | http://<ip>/action/getSystemConfig?name=DevStorage |
| --- | --- |
| Comment |  |
| Response | Device.Redundancy=1 Device.OverWriteSwitch=1 Device.OverWritePeriod=6 Device.OverWriteMode=1 |

### 11.2.2 SetDevStorageConfig

| URL Syntax | http://<ip>/action/setSystemConfig?name=DevStorage&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or Error |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Device.Redundancy | integer | Each bit represent a disk attribute. 0: main disk, 1: sub disk. |
| Device.OverWriteSwitch | char | 0:close, 1: open. |
| Device.OverWritePeriod | char | Overwrite period. unit is hour. |
| Device.OverWriteMode | char | Overwrite mode. 0: by hour, 1: by day. |

# 12. Advance

## 12.1 IP Filter

### 12.1.1 GetIPFilterConfig

| URL Syntax | http://<ip>/action/getSysConfig?name=IPFilter |
| --- | --- |
| Comment | FilterNo below is the banned IP list index. Valid value range is [0 ~ 15]. |
| Response | IPFilter.Switch=1 IPFilter.Filtered[FilterNo ].IPAddress=192.168.1.111 IPFilter.Filtered[FilterNo ].Enable=1 |

### 12.1.2 SetIPFilterConfig

| URL Syntax | http://<ip>/action/setConfig?name=IPFilter&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | FilterNo is the banned IP list index. Valid value range is [0 ~ 15]. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| IPFilter.Switch | char | Enable/Disable access filter function. |
| IPFilter.Filtered[FilterNo ].IPAddress | string | Filtered IP address. Max length: 32. |
| IPFilter.Filtered[FilterNo ].Enable | char | Filtered IP address switch. 0: disable, 1: enable. |

## 12.2 FtpUpgrade

### 12.2.1 GetFtpUpgradeConfig

| URL Syntax | http://<ip>/action/getConfig?name=FtpUpgrade |
| --- | --- |
| Comment | Current not support. |
| Response | FtpUpgrade.IPAddress=192.168.1.109 FtpUpgrade.UserName=admin FtpUpgrade.Password=123456 FtpUpgrade.FtpPath=upgrade FtpUpgrade.ProductName=rs-ipc FtpUpgrade.Port=21 FtpUpgrade.Switch=1 FtpUpgrade.Tips=0 |

### 12.2.2 SetFtpUpgradeConfig

| URL Syntax | http://<ip>/action/setConfig?name=FtpUpgrade&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| FtpUpgrade.IPAddress | string | FTP IP Address. Max length: 32. |
| FtpUpgrade.UserName | string | FTP user name. Max length: 32. |
| FtpUpgrade.Password | string | FTP user password. Max length: 32. |
| FtpUpgrade.FtpPath | string | FTP upgrade path. Max length: 64. |
| FtpUpgrade.ProductName | string | Product name. Max length: 32. |
| FtpUpgrade.Port | short | FTP port. |
| FtpUpgrade.Switch | char | Enable/Disable Ftp upgrade function. |
| FtpUpgrade.Tips | char | FTP upgrade tips. |

## 12.3 HttpUpgrade

### 12.3.1 GetHttpUpgradeConfig

| URL Syntax | http://<ip>/action/getConfig?name=HttpUpgrade |
| --- | --- |
| Comment | Current not support. |
| Response | HttpUpgrade.Port=80 HttpUpgrade.Addr=192.168.1.129 HttpUpgrade.Path=/upgrade/ |

### 12.3.2 SetHttpUpgradeConfig

| URL Syntax | http://<ip>/action/setConfig?name=HttpUpgrade&<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment | Current not support. |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| HttpUpgrade.Port | int | HTTP port. |
| HttpUpgrade.Addr | string | HTTP IP Address. Max length: 64. |
| HttpUpgrade.Path | string | HTTP path. Max length: 128. |

## 12.4 ParamDefault

### 12.4.1 ColorDefault

| URL Syntax | http://<ip>/action/colorDefault? |
| --- | --- |
| Comment |  |
| Response | Color.Brightness=128 Color.Contrast=128 Color.Hue=128 Color.Saturation=128 Color.Sharpness=128 |

### 12.4.2 ImageDefault

| URL Syntax | http://<ip>/action/imageDefault? |
| --- | --- |
| Comment |  |
| Response | Camera.IRCutMode=0 Camera.IRCutDelay=2 Camera.IRCutSensitive=1 Camera.Mirror=0 Camera.Flip=0 Camera.Rotate=0 Camera.BackLightMode=1 Camera.BackLightLevel=1 Camera.R3dnrMode=1 Camera.R3dnrThreshTarget=128 Camera.DISEnable=1 Camera.DefogMode=1 Camera.DefogStrength=128 Camera.DwdrMode=1 Camera.DwdrStrength=128 Camera.GainControlMode=2 Camera.WBMode=0 Camera.Rgain=128 Camera.Ggain=128 Camera.Bgain=128 Camera.ShutterMode=0 Camera.ShutterSpeed=25 Camera.FlickerCtrl=0 |

## 12.5 System Operation

### 12.5.1 Reboot

| URL Syntax | http://<ip>/action/reboot? |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

### 12.5.2 LoadDefault

| URL Syntax | http://<ip>/action/loadDefault?<paramName>=<paramValue>[&<paramName>=<paramValue>...] |
| --- | --- |
| Comment |  |
| Response | OK or ERROR |

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Default.DisplayFlag | char | Display page default flag. 0 :disable; 1 : enable. |
| Default.RecordFlag | char | Record page default flag. 0 :disable; 1: enable. |
| Default.NetworkFlag | char | Network page default flag. 0 :disable; 1 : except network setting parameter; 2 : enable all. |
| Default.AlarmFlag | char | Alarm page default flag. 0 :disable; 1 : enable. |
| Default.DeviceFlag | char | Device page default flag. 0 :disable; 1 : enable. |
| Default.SystemFlag | char | System page default flag. 0 : disable; 1 :enable. |
| Default.AdvanceFlag | char | Advance page default flag. 0 : disable; 1 : enable. |

# 13. Events

## 13.1 EventHandler

### 13.1.1 SubscribeEvent

| URL Syntax | http://<ip>/action/eventManage?name=Subscribe |
| --- | --- |
| Comment | EventType value range is [1 ~ 4]. 1 : motion detect 2 : Lens block 3 : Storage abnormal 4 : network abnormal Status value range is {0, 1}. 1 : event start 0 : event stop |
| Response | EventType=1, Status=1, TriggerTime=2015-05-27 16:40:23 |

### 13.1.2 UnSubscribeEvent

| URL Syntax | http://<ip>/action/eventManage?name=UnSubscribe |
| --- | --- |
| Comment | OK means stop receive event data. |
| Response | OK or ERROR |