MERX NVR/DVR/IPC HTTP API 1.1

1. 获取设备信息（GetDeviceInfo ）	7

1.1 请求格式	7

1.2返回格式	7

2 . eventManage  (事件订阅和上报)	11

2.1 订阅事件的请求格式	11

2.2 订阅事件的回应格式	11

2.3上报事件报警格式	12

2.4 取消订阅事件的请求格式	14

3. 云台控制（PTZControl）	14

3.1 请求格式：	14

3.2 格式说明：	15

3.3 回应消息：	15

4. 预览和回放	16

4.1 RTSP预览url规则	16

4.2 RTSP回放url规则	16

4.3 Http预览规则	16

5. 日志搜索	17

5.1 请求格式	17

5.2 回应格式	17

5.3 参数说明	18

6. 录像搜索	21

6.1 请求格式	21

6.2 回应格式	22

6.3 参数说明	22

7. 下载录像文件	23

7.1 请求格式	23

7.2 回应格式	23

7.3 参数说明	23

8. 镜头参数	23

8.1参数获取请求格式：	23

8.2参数获取回应格式：	24

8.3参数设置请求格式：	25

8.4 参数设置回应格式：	26

8.5 参数说明：	26

9. 视频彩色参数	28

9.1参数获取请求格式：	28

9.2参数获取回应格式：	28

9.3参数设置请求格式：	29

9.4 参数设置回应格式：	29

9.5 参数说明：	29

10. Live	29

10.1参数获取请求格式：	29

10.2参数获取回应格式：	30

10.3参数设置请求格式：注：设置尚未实现	30

10.4 参数设置回应格式：	30

10.5 参数说明：	30

11. OSD	31

11.1参数获取请求格式：	31

11.2参数获取回应格式：	31

11.3参数设置请求格式：	32

11.4 参数设置回应格式：	32

12.5 参数说明：	33

12. VideoCover	33

12.1参数获取请求格式：	33

12.2参数获取回应格式：	33

12.3参数设置请求格式：	35

12.4 参数设置回应格式：	35

12.5 参数说明：	35

13. ROI	35

13.1参数获取请求格式：	35

13.2参数获取回应格式：	36

13.3参数设置请求格式：	37

13.4 参数设置回应格式：	38

13.5 参数说明：	38

14. StreamUri	38

14.1参数获取请求格式：	38

14.2参数获取回应格式：	39

14.3 参数说明：	39

15. MainStream	39

15.1参数获取请求格式：	39

15.2参数获取回应格式：	40

15.3参数设置请求格式：	41

15.4 参数设置回应格式：	41

15.5 参数说明：	41

16. SubStream	42

16.1参数获取请求格式：	42

16.2参数获取回应格式：	43

16.3参数设置请求格式：	43

16.4 参数设置回应格式：	44

16.5 参数说明：	44

17. MobileStream	45

17.1参数获取请求格式：	45

17.2参数获取回应格式：	45

17.3参数设置请求格式：	46

17.4 参数设置回应格式：	47

17.5 参数说明：	47

18. Audio	48

18.1参数获取请求格式：	48

18.2参数获取回应格式：	48

18.3参数设置请求格式：	49

18.4 参数设置回应格式：	49

18.5 参数说明：	50

19.NetWork	50

19.1参数获取请求格式：	50

19.2参数获取回应格式：	50

19.3参数设置请求格式：	51

19.4 参数设置回应格式：	51

19.5 参数说明：	51

20.DDNS	52

20.1参数获取请求格式:	52

20.2参数获取回应格式：	52

20.3参数设置请求格式：	52

20.4 参数设置回应格式：	53

20.5 参数说明：	53

21.Email	53

21.1参数获取请求格式:	53

21.2参数获取回应格式：	53

21.3参数设置请求格式：	54

21.4 参数设置回应格式：	54

21.5 参数说明：	54

22.P2P	55

23.1参数获取请求格式:	55

22.2参数获取回应格式：	55

22.3参数设置请求格式：	55

22.4 参数设置回应格式：	55

22.5 参数说明：	56

23.RTSP	56

23.1参数获取请求格式	56

23.2参数获取回应格式：	56

23.3参数设置请求格式：	56

23.4 参数设置回应格式：	56

23.5 参数说明：	57

24. FTP	57

24.1参数获取请求格式	57

24.2参数获取回应格式：	57

24.3参数设置请求格式：	58

24.4 参数设置回应格式：	58

24.5 参数说明：	58

25. IOAlarm	59

25.1参数获取请求格式：	59

25.2参数获取回应格式：	59

25.3参数设置请求格式：	60

25.4 参数设置回应格式：	60

25.5 参数说明：	60

26. Motion	61

26.1参数获取请求格式：	61

26.2参数获取回应格式：	61

26.3参数设置请求格式：	62

26.4 参数设置回应格式：	62

26.5 参数说明:	63

27. PerimLine	63

27.1参数获取请求格式：	63

27.2参数获取回应格式：	64

27.3参数设置请求格式：	65

27.4 参数设置回应格式：	66

27.5 参数说明:	66

28. Perimeter	67

28.1参数获取请求格式：	67

28.2参数获取回应格式：	67

28.3参数设置请求格式：	69

28.4 参数设置回应格式：	69

28.5 参数说明:	69

29. SODAlarm	70

29.1参数获取请求格式：	70

29.2参数获取回应格式：	70

29.3参数设置请求格式：	72

29.4 参数设置回应格式：	72

29.5 参数说明:	72

30. PDAlarm	73

30.1参数获取请求格式：	73

30.2参数获取回应格式：	74

30.3参数设置请求格式：	75

30.4 参数设置回应格式：	75

30.5 参数说明:	76

31. FDAlarm	77

31.1参数获取请求格式：	77

31.2参数获取回应格式：	77

31.3参数设置请求格式：	78

31.4 参数设置回应格式：	79

31.5 参数说明:	79

32. CCAlarm	80

32.1参数获取请求格式：	80

32.2参数获取回应格式：	80

32.3参数设置请求格式：	82

32.4 参数设置回应格式：	82

32.5 参数说明:	82

33. ODAlarm	83

33.1参数获取请求格式：	83

33.2参数获取回应格式：	83

33.3参数设置请求格式：	84

33.4 参数设置回应格式：	84

33.5 参数说明:	84

34. GeneralRec	85

34.1参数获取请求格式：	85

34.2参数获取回应格式：	85

34.3参数设置请求格式：	86

34.4 参数设置回应格式：	86

34.5 参数说明:	86

35. SmartRec	87

35.1参数获取请求格式：	87

35.2参数获取回应格式：	87

35.3参数设置请求格式：	87

35.4 参数设置回应格式：	88

35.5 参数说明:	88

36. Schedule	88

36.1参数获取请求格式：	88

36.2参数获取回应格式：	88

36.3参数设置请求格式：	89

36.4 参数设置回应格式：	90

36.5 参数说明:	90

37. System	91

37.1参数获取请求格式:	91

37.2参数获取回应格式：	91

37.3参数设置请求格式：	91

37.4 参数设置回应格式：	91

37.5 参数说明：	92

38. User	92

38.1参数获取请求格式:	92

38.2参数获取回应格式	92

38.3参数获取请求格式：	93

38.4参数获取请求格式：	93

38.5参数设置请求格式：	94

38.6 参数设置回应格式：	94

38.7 参数说明：	95

39. NTP	95

39.1参数获取请求格式:	95

39.2参数获取回应格式：	95

39.3参数设置请求格式：	96

39.4 参数设置回应格式：	96

39.5 参数说明：	96

40. DST	97

40.1参数获取请求格式:	97

40.2参数获取回应格式：	97

40.3参数设置请求格式：	98

40.4 参数设置回应格式：	98

40.5 参数说明：	98

41. Device	99

41.1参数获取请求格式:	99

41.2参数获取回应格式：	99

41.3参数设置请求格式：	99

41.4 参数设置回应格式：	100

41.5 参数说明：	100

42. Device Storage	100

42.1参数获取请求格式:	100

42.2参数获取回应格式：	100

42.3参数设置请求格式：	101

42.4 参数设置回应格式：	101

42.5 参数说明：	101

43. IP Filter	102

43.1参数获取请求格式:	102

43.2参数获取回应格式：	102

43.3参数设置请求格式：	102

43.4 参数设置回应格式：	102

43.5 参数说明：	103

44. ColorDefault	103

44.1请求格式:	103

44.2回应格式：	103

45. imageDefault	103

45.1请求格式:	103

45.2回应格式：	103

46. Reboot	104

46.1请求格式:	104

46.2回应格式：	104

47. LoadDefault	105

47.1请求格式:	105

47.2回应格式：	105

48. shot	105

48.1请求格式：	105

48.2回应格式：	106

48.3参数说明：	106

49. custom parameter	106

49.1保存参数请求格式：	106

49.2 获取参数请求格式	106

49.3 回应格式：	107

50. AlarmOut	107

50.1 请求格式：	107

50.2 格式说明：	107

50.3 回应消息：	107

51. ACCESSTKOEN	108

51.1请求格式：	108

51.2 回应消息：	108

52. 智能分析（获取Cross Counting 和 Line Crossing数据）	108

52.1请求格式：	109

52.2 回应消息：	109

52.3 参数说明：	109

53. OSDS	110

53.1参数获取请求格式：	110

53.2参数获取回应格式：	110

53.3参数设置请求格式：	111

53.4 参数设置回应格式：	111

53.5 参数说明：	111

# 1. 获取设备信息（GetDeviceInfo ）

1.1 请求格式

GET /action/getDeviceInfo HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

1.2返回格式

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: 4620

{

"connectUsers":	0,

"connectMode":	"CLOUD",

"Channel":	[{

"channel":	0,

"activeConnect":	true,

"audioSwitch":	true,

"channelName":	"CH1",

"mainstream_fps":	15,

"mainstream_kbps":	4096,

"mainstream_width":	1920,

"mainstream_height":	1080,

"substream_fps":	4,

"substream_kbps":	64,

"substream_width":	352,

"substream_height":	288,

"motion_status":	false,

"videoLoss":	false,

"record_status":	true,

"terminal_device_mac":	"00-12-35-fd-ae-26",

"MainStreamURL":	"rtsp://192.168.6.67:554/ch01/0",

"SubStreamURL":	    "rtsp://192.168.6.67:554/ch01/1",

"MobileStreamURL":	"rtsp://192.168.6.67:554/ch01/2"

}, {

"channel":  1,

"activeConnect":	false,

"audioSwitch":	true,

"channelName":	"CH2",

"mainstream_fps":	15,

"mainstream_kbps":	4096,

"mainstream_width":	1920,

"mainstream_height":	1080,

"substream_fps":	4,

"substream_kbps":	64,

"substream_width":	352,

"substream_height":	288,

"motion_status":	false,

"videoLoss":	true,

"record_status":	false,

"terminal_device_mac":	"00-12-35-fd-ae-26",

"MainStreamURL":	"rtsp://192.168.6.67:554/ch02/0",

"SubStreamURL":	    "rtsp://192.168.6.67:554/ch02/1",

"MobileStreamURL":	"rtsp://192.168.6.67:554/ch02/2"

}, {

"channel":  2,

"activeConnect":	true,

"audioSwitch":	true,

"channelName":	"CH3",

"mainstream_fps":	15,

"mainstream_kbps":	4096,

"mainstream_width":	1920,

"mainstream_height":	1080,

"substream_fps":	4,

"substream_kbps":	64,

"substream_width":	352,

"substream_height":	288,

"motion_status":	false,

"videoLoss":	false,

"record_status":	true,

"terminal_device_mac":	"00-12-35-fd-ae-26",

"MainStreamURL":	"rtsp://192.168.6.67:554/ch03/0",

"SubStreamURL":	    "rtsp://192.168.6.67:554/ch03/1",

"MobileStreamURL":	"rtsp://192.168.6.67:554/ch03/2"

}, {

"channel":  3,

"activeConnect":	true,

"audioSwitch":	true,

"channelName":	"CH4",

"mainstream_fps":	15,

"mainstream_kbps":	4096,

"mainstream_width":	1920,

"mainstream_height":	1080,

"substream_fps":	4,

"substream_kbps":	64,

"substream_width":	352,

"substream_height":	288,

"motion_status":	false,

"videoLoss":	false,

"record_status":	true,

"terminal_device_mac":	"00-12-35-fd-ae-26",

"MainStreamURL":	"rtsp://192.168.6.67:554/ch04/0",

"SubStreamURL":	    "rtsp://192.168.6.67:554/ch04/1",

"MobileStreamURL":	"rtsp://192.168.6.67:554/ch04/2"

}

}],

"ddnsHostName":	"",

"deviceID ":	0,

"deviceIp":	"172.18.12.96",

"deviceName":	"1080P-HY04N",

"deviceModel":	"HY-DVR",

"gatewayAddr":	"172.18.0.1",

"hostName":	"HY-DVR-",

"httpPort":	80,

"macAddress":	"00-10-22-72-49-01",

"p2pHostName":	"RSVT1507000003172",

"p2pStatus":	false,

"rtspPort":	554,

"HddNumbers":	2,

"HddInfo":	[{

"id":	1,

"active":	1,

"status":	4,

"totalSize":	953869,

"freeSize":	0,

"freeTime":	0,

"GroupNr":	0,

"model":	"WDC",

"fw_rev":	"01.01A01WD-WCC1U3387863",

"serial_no":	"WD-WCC1U3387863",

"hddtype":	0

}, {

"id":	1,

"active":	0,

"status":	4,

"totalSize":	305245,

"freeSize":	0,

"freeTime":	0,

"GroupNr":	0,

"model":	"WDC",

"fw_rev":	"01.01A01WD-WX21A4046399",

"serial_no":	"WD-WX21A4046399",

"hddtype":	0

}],

"timeZone":  9      (-12~+13)

}

# 2 . eventManage  (事件订阅和上报)

2.1 订阅事件的请求格式

POST /action/eventManage HTTP/1.1

Host: 172.18.12.96

Authorization: Digest username="xx",realm="xx",qop="auth",nonce="xx",uri="path",cnonce="xx",nc=00000001,response="xx",opaque="x"

Content-Type: application/json

Content-Length: 100

{

"name":"Subscribe",

"ip":"172.18.1.26",

"port":5330,

"chid": 1,

"customflag":1

}

参数说明：

name:  Subscribe表示订阅事件，unSubscribe 表示取消订阅.

ip: 订阅事件的ip.

port: 订阅事件的port，如果发送了订阅请求，会将事件发送到对应的订阅ip和port.

chid: 通道号或者摄像机编码.

customflag: 具体的定制服务，不同的值代表不同的服务，具体如下：

1：表示要往服务器发送I/O报警事件的图片。

其他值暂时未定义。

2.2 订阅事件的回应格式

订阅成功：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"

}

订阅失败：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "failed",

"reason":"DSP"

}

2.3上报事件报警格式

2.3.1 告警消息格式

POST /action/eventManage HTTP/1.1

Host: 172.18.6.42

Connection: close

Content-Type: application/json

Content-Length: xx

{

"eventType":1,

"status":2,

"channel":1,

"triggerTime":" 2016-07-28 18:25:10"

"id":123456,

"chid":1

}

参数说明：

EventType: 报警类型

typedef enum{

INTF_IO_ALARM_E= 0,        	//I/O探头告警

INTF_MOTION_ALARM_E,       	//移动侦测告警

INTF_AI_ALARM_E,  			//周界拌线告警

INTF_AVD_ALARM_E,  		 	//视频诊断告警

INTF_AI_RULE_E,  	 	//周界拌线规则上报告警

INTF_VIDEOLOSS_ALARM_E, 		//视频丢失告警

INTF_HDD_ALARM_E,          	//硬盘告警

INTF_DEVSTATUS_REPORT_E = 8,    //设备状态上告

INTF_TELMODULE_ALARM_E,         //电话报警

INTF_MDVR_ALARM_E,     		//车载设备状态上告

INTF_ICCARD_ALARM_E,     	//IC设备状态上告

INTF_RECORDSTATUS_ALARM_E, //录像状态告警

INTF_HDDSTATUS_ALARM_E,    //硬盘状态告警

INTF_FTPUPGRADE_ALARM_E,   //Ftp远程升级告警

INTF_VIDEO_HIDE_ALARM_E = 18,   //视频遮挡报警

INTF_OSC_ALARM_E,

INTF_PEA_ALARM_E,          //周界伴线告警

INTF_OSCRULE_ALARM_E,      //物品遗留告警

INTF_KGALARM_PUSH_E,       //Kguard alarm push

INTF_KG_IPN_ALARM_E ,     //kguard iPN Alarm push

INTF_RECORD_FLAG_ALARM_E,

INTF_IPC_PEALINE_ALARM_E,   //ipc 周界伴线告警 2015.11.30

INTF_IPC_PEAAREA_ALARM_E,   //ipc 周界告警     2015.11.30

INTF_IPC_OSC_ALARM_E ,

INTF_IPC_HD_ALARM_E,         //ipc 人体检测告警 2016.03.07

INTF_IPC_FD_ALARM_E,         //ipc 人脸检测告警 2016.03.07

INTF_IPC_PCC_ALARM_E,        //ipc 过线统计告警 2016.03.07

INTF_IPC_MANAGE_ALARM_E,	 //ipc 人体，人脸，过线统计事件发生和结束事件

INTF_SENSORSTATUS_ALARM_E,

INTF_FISHEYE_IPC_STATE_E,

INTF_PTZ_IPC_ALARM_E,

INTF_PIR_ALARM_E,			//红外传感告警开始

INTF_JDVCA_ALARM_E,         //用于IPC将98C处理后的告警信息发送给南瑞电网平台

INTF_MOTION_SMART_E,

INTF_LOWPOWER_E,

INTF_POWER_CHANGE,

INTF_CHARGE_POWER,

INTF_NAME_CHANGE,

INTF_DEVNAME_CHANGE,

INTF_DEVPARAM_CHANGE,

} EventType;

status:报警状态

1 : event start

0 : event stop

channel：通道号

triggerTime: 事件发生的时间，例如：2016-07-28 18:25:10

id：一般为p2p id号

chid: 摄像头id

2.3.2 事件抓图格式

POST /action/eventManage HTTP/1.1

Host: 172.18.6.42

Connection: close

Content-Type: application/json

Content-Length: xx

{

"id":123456,

"imageType":1,

"imageName":"2017-11-24 08:09:11.jpg",

"imageBase64":"iVBORw0KGgoAAAANSUhEUgAAABQAAAAUCAYAAACNiR0NAAAAGXRFWHRTb2Z0d2FyZQBBZG9iZSBJbWFnZVJlYWR5ccllPAAAAWdJREFUeNpi/P///xMGBgZpBuqAp4xAA/8DGcuAeDcQM5JpEMgMCyBOZ/gPAR4gcynEhiCDmKA2SOKx3QuIg4hwpSyIYCFC4VYoTVRwMBGQ10Jiy1DDQF8ktjkpBv7FIR+NxLZDYpdiCVeIGdBYDsASayJQuX4gPgnE76HibP8RwAhJvfV/KOMzEH8A4ntAXIukIAOqSQCIG6FskLj9f1RwH4gfAPFLkFkwL/8AYhEgbgLicqhYApT+AMSXoGwxIPaHsp2B+DQQ8wMxNxBzIXvZDWr7QSi/AIh/A/F+qLgyVHwWED8D4otYgsgB5gUQSECSOIfknWCoGCPUSzCQhMVAT+ScwoiWPN5D2buQ8uoBJDWbsKQIVlzp8DcQ6wCxIxB/RhI/B6VB4fYGVzrElfWeQTEygLlwN76EzUJCEXUKGvO7iDHwJZFl3kI88s+RDQwAYmYKC1hw1gQlh6dAWopKVcAzgAADAMJohSLllJKHAAAAAElFTkSuQmCC"

}

参数说明：

id：一般为p2p id号

imageType: 图片类型，如0 : jpeg； 1 : png；

imageName: 图片名称， 如 2017-11-24 08:09:11.jpg

imageBase64: 图片base64编码

2.4 取消订阅事件的请求格式

POST /action/eventManage HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-Type: application/json

Content-Length: 100

{

"name":"unSubscribe",

"ip":"172.18.1.26",

"port":5330

}

3. 云台控制（PTZControl）

3.1 请求格式：

GET /action/PtzControl HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

"action":  "string",   //"start"/"stop"

"channel" :  1,

"command": 1,

"speed" :  1     当"name" = "move"

}

3.2 格式说明：

channel:表示通道号或者摄像机ID号

speed: 表示速度，//1-8 (1 slow, 8 fast)。

command 表示操作命令，具体对应值如下表格：

| 定义 | 值 | 描述 |
| --- | --- | --- |
| MsgPTZUp | 1 | 向上转动 |
| MsgPTZDown | 2 | 向下转动 |
| MsgPTZLeft | 3 | 向左转动 |
| MsgPTZRight | 4 | 向右转动 |
| MsgPTZUpLeft | 5 | 向左上转动 |
| MsgPTZUpRight | 6 | 向右上转动 |
| MsgPTZDownLeft | 7 | 向左下转动 |
| MsgPTZDownRight | 8 | 向右下转动 |
| MsgPTZZoomIn | 11 | 焦距变大 |
| MsgPTZZoomOut | 12 | 焦距变小 |
| MsgPTZFocusNear | 13 | 焦点前调 |
| MsgPTZFocusFar | 14 | 焦点后调 |
| MsgPTZIRISOpen | 15 | 光圈扩大 |
| MsgPTZIRISClose | 16 | 光圈缩小 |
| MsgPTZAutoScan | 21 | 自动扫描 |
| MsgPTZCruise | 51 | 自动巡航 |
| MsgPTZGuard | 90 | 守护 |
| MsgPTZSetPreset | 91 | 设置预置点 |
| MsgPTZClearPreset | 92 | 清除预置点 |
| MsgPTZCallPreset | 93 | 前往预置点 |
| MsgPTZSensorPresetInfoGet | 94 | 获取预置点信息 |
| MsgPTZSensorPresetInfoSet | 95 | 设置预置点信息 |
| MsgPTZLockFocus | 96 |  |
| MsgPTZLineScanA | 98 |  |
| MsgPTZLineScanB | 99 |  |

3.3 回应消息：

3.3.1成功回应

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"

}

3.3.2失败回应

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "failed",

"reason":"DSP"

}

4. 预览和回放

4.1 RTSP预览url规则

url形式：

rtsp://ip:port/chA/B

其中B表示流类型，取值范围：0 表示主码流， 1表示子码流， 2手机码流。

其中A表示设备通道号，取值范围：1-255的整数。

4.2 RTSP回放url规则

url形式：

rtsp://192.168.1.168:554/cam/playback?channel=01&starttime=2016-8-31T17:13:12Z&endtime=2016-8-31T17:28:49Z

其中starttime表示开始播放的时间点（UTC时间）。

其中endtime表示结束播放的时间点（UTC时间）。

其中channel表示设备通道号，取值范围：1-255的整数。

4.3 Http预览规则

请求格式：

GET /action/preview HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

"channel":1,

"streamType":0,

}

回应格式：

HTTP/1.1 200 OK

Connection: keep-alive

Content-Type: chunked

\r\ndatasize\r\n

H264/h265 data

\r\ndatasize\r\n

H264/h265 data

…

\r\n0\r\n

5. 日志搜索

5.1 请求格式

GET /action/ getsyslog HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

"maintype":1,

"startTime":rtctime,

"endTime":rtctime,

"logMax":500

}

5.2 回应格式

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"logIndex":

[

{

"maintype":1,

"subtype":2,

"channel":1,

"Time":"2016-11-10-15-20-2",

"describe":"string"

},

….

{

"maintype":5,

"subtype":2,

"channel":31,

"Time":"2016-11-10-15-20-2",

"describe":"string"

}

]

}

5.3 参数说明

logMax: 表示要发送的最大日志条数。

endTime  startTime : 2016-1-1-15-20-2

Maintype: 主日志类型，如下取值：

typedef enum _NET_LOG_TYPE_E_

{

NET_LT_SYSTEM = 0,

NET_LT_CONFIG,

NET_LT_ALARM,

NET_LT_ACCOUNT,

NET_LT_RECORD,

NET_LT_STORAGE,

NET_LT_PTZ,

NET_LT_ALL

}NET_LOG_TYPE_E;

Subtype: 子类型，取值如下：

typedef enum _NET_SYSTEM_LOG_TYPE_E_

{

NET_SLT_STARTUP,

NET_SLT_SHUTDOWN,

NET_SLT_REBOOT,

NET_SLT_AUTOMAINTAIN,

NET_SLT_UPGRADE

}NET_SYSTEM_LOG_TYPE_E;

typedef enum _NET_PTZ_LOG_TYPE_E_

{

NET_PLT_MOVE,

NET_PLT_ZOOM,

NET_PLT_FOCUS,

NET_PLT_IRISOPEN,

NET_PLT_IRISCLOSE,

NET_PLT_AUTOSCAN,

NET_PLT_CRUISE,

NET_PLT_SETPRESET,

NET_PLT_CLRPRESET,

NET_PLT_CALLPRESET,

}NET_PTZ_LOG_TYPE_E;

typedef enum _NET_CONFIG_LOG_TYPE_E_

{

NET_CLT_INVALID,

/*各个参数设置页面*/

NET_CLT_SYSSET,		//系统参数设置

NET_CLT_RECSET,		//录像设置

NET_CLT_OSDSET,		//前端OSD 设置

NET_CLT_USERSET,

NET_CLT_ALARMSET,

NET_CLT_RECMODE,

NET_CLT_CLRSET,		/*color*/

NET_CLT_MDSET,

NET_CLT_COVERSET,

NET_CLT_PTZSET,

NET_CLT_NETSET,

NET_CLT_DDNSSET,

NET_CLT_TIMESET,

NET_CLT_RTSPSET,

NET_CLT_LANGTAOSET,

NET_CLT_MOBILESET,

NET_CLT_WCDMA,

NET_CLT_WIFISET,

NET_CLT_EMAILSET,

NET_CLT_STATE,

NET_CLT_NTPSET,

NET_CLT_CAMERASET,

NET_CLT_MOBILESTREAMSET,

NET_CLT_SUBSTREAMSET,

NET_CLT_MAINSTREAMSET,

NET_CLT_IPFILTER,

NET_CLT_FTPSET,

NET_CLT_PLATFORMPARA,

NET_CLT_SCHEDULE,

NET_CLT_PPPOE,

NET_CLT_DISKSET,

NET_CLT_SERIAL,

NET_CLT_GENERAL,

NET_CLT_DSTSET,

NET_CLT_MAINTAIN,

NET_CLT_ABNORMAL,

NET_CLT_DEFALUTEALL,

NET_CLT_INTELLIGENT,

NET_CLT_INTAVD,

NET_CLT_EMAILSCHEDULE,

NET_CLT_IPC,

NET_CLT_IPCIOALARM,

NET_CLT_ROUTERLAN,

NET_CLT_ROUTERWAN,

NET_CLT_IPCWIFI,

NET_CLT_VEHICLEMNG,

NET_CLT_OUTPUT,

NET_CLT_TELALARM_AREA,

NET_CLT_ALARM_WIRE_SENSOR,

NET_CLT_TELALARM_WIRELESS_SENSOR,

NET_CLT_PHONE_NUMBER_SET,

NET_CLT_HUAWEI_PLATFORM,

NET_CLT_ELECLOCK,

NET_CLT_CLOUDSTORAGE,

NET_CLT_CLOUDEMAIL,

NET_CLT_P2PMOBILE,

NET_CLT_DEVALLSTATUSSET,

NET_CLT_IPCROI,

NET_CLT_VOICE_SET,

NET_CLT_VIDEO_BLIND,

NET_CLT_MAX_NUM

/* ......*/

}NET_CONFIG_LOG_TYPE_E;

typedef enum _NET_ALARM_LOG_TYPE_E_

{

NET_ALT_MOTION,

NET_ALT_IO,

NET_ALT_VIDOE_LOSS

}NET_ALARM_LOG_TYPE_E;

typedef enum _NET_ACCOUNT_LOG_TYPE_E_

{

NET_ATLT_LOGIN,

NET_ATLT_LOGOUT,

NET_ATLT_ADD,

NET_ATLT_DEL,

NET_ATLT_MODIFY

}NET_ACCOUNT_LOG_TYPE_E;

typedef enum _NET_RECORD_LOG_TYPE_E_

{

NET_RLT_START_SCHEDULE,

NET_RLT_START_MANUAL,

NET_RLT_STOP,

NET_RLT_SEARCH,

NET_RLT_PLAYBACK,

NET_RLT_BACKUP,

NET_RLT_DOWNLOAD,_

}NET_RECORD_LOG_TYEP_E;

typedef enum _NET_STORAGE_LOG_TYPE_E_

{

NET_STLT_FORMAT,

NET_STLT_HDD_NOSPACE,

NET_STLT_HDD_ERR,

NET_STLT_AUTO_COVER,/*自动覆盖*/

NET_STLT_CHANGE_PARTITION

}NET_STORAGE_LOG_TYPE_E;

6. 录像搜索

6.1 请求格式

GET /action/ getRecordList HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

"Channel":

[0, 1,2,255],

"recType":1,

"streamType":0,

"startTime":rtctime,

"endTime":rtctime,

"recordMax":500

}

6.2 回应格式

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"recordlist":

[

{

"recType":1,

"channel":1,

"streamType":0,

"startTime":"2016-1-1-15-20-2",

"endTime":"2016-1-1-15-25-2",

"size": 1024 ,//字节

},

….

{

"recType":1,

"channel":1,

"streamType":1,

"startTime": "2016-11-10-15-20-2",

"endTime": "2016-11-10-15-23-2",

"size": 1024 ,//字节

}

]

}

6.3 参数说明

Channel：表示通道(最大256通道)。

endTime  startTime : 2016-1-1-15-20-2(录像事件的设备实际时间)

streamType: 0:主码流，1：子码流

recType: 录像类型，取值如下：

#define REC_NORMAL          (1<<0)

#define REC_MDALARM         (1<<1)

#define REC_IOALARM         (1<<2)

#define AllRecord         0xFFFFFFFF

7. 下载录像文件

7.1 请求格式

GET /action/recordDownload HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

"channel":1,

"streamType":0,

" recType ":0,

"startTime":rtctime,

"endTime":rtctime,

}

7.2 回应格式

HTTP/1.1 200 OK

Connection: keep-alive

Content-Type: chunked

\r\ndatasize\r\n

H264/h265 data

\r\ndatasize\r\n

H264/h265 data

…

\r\n0\r\n

7.3 参数说明

streamType ：0 表示主码流，1表示子码流

endTime  startTime : 2016-1-1-15-20-2(设备端实际时间)

8. 镜头参数

8.1参数获取请求格式：

POST /action/getConfig/Camera HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

8.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"IRCutMode"：0，

"IRCutDelay"：3，

"IRCutSensitive"：1，

"IRFuncType"：0，

"Mirror"：0,

"Flip":0,

"Rotate":0,

"BackLightMode":1,

"BackLightLevel":1,

"R3dnrMode":1,

"R3dnrThreshTarget":50,

"DISEnable":1,

"DefogMode":1,

"DefogStrength":128,

"DwdrMode":1,

"DwdrStrength":50,

"GainControlMode":2,

"WBMode":0,

"Rgain":50,

"Ggain":50,

"Bgain":50,

"ShutterMode":0,

"ShutterSpeed":25,

"FlickerCtrl":0

},

{

"channel":2,

"IRCutMode"：0，

"Camera.IRCutDelay"：3，

"Camera.IRCutSensitive"：1，

"Camera.IRFuncType"：0，

"Camera.Mirror"：0,

"Camera.Flip":0,

"Camera.Rotate":0,

"Camera.BackLightMode":1,

"Camera.BackLightLevel":1, "IRCutMode"：0，

"IRCutDelay"：3，

"IRCutSensitive"：1，

"IRFuncType"：0，

"Mirror"：0,

"Flip":0,

"Rotate":0,

"BackLightMode":1,

"BackLightLevel":1,

"R3dnrMode":1,

"R3dnrThreshTarget":50,

"DISEnable":1,

"DefogMode":1,

"DefogStrength":128,

"DwdrMode":1,

"DwdrStrength":50,

"GainControlMode":2,

"WBMode":0,

"Rgain":50,

"Ggain":50,

"Bgain":50,

"ShutterMode":0,

"ShutterSpeed":25,

"FlickerCtrl":0

}]

}

8.3参数设置请求格式：

POST /action/setConfig/camera HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和8.2中参数获取回应的json格式一致

}

8.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

8.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| chmask | Unsigned int 数组 | 表示要获取的通道所对应的掩码值，数组下标0-8，chmask[0]:表示1-32通道对应的掩码，以此类推。 |
| IRCutMode | char | Range is {0, 1, 2, 3} 0 – auto. 1 – day. 2- night. 3 – video auto |
| IRCutDelay | char | Range is [0 ~ 36]. unit : second |
| IRCutSensitive | char | Range is {0, 1, 2} 0: High. 1: Middle. 2: Low. |
| IRFuncType | char | Infrared function switch. 0: close, 1: auto. 注：IPC不支持 |
| Mirror | char | Range is {0, 1}. Flip Horizontal 0: close. 1: open. |
| Flip | char | Range is {0, 1}. Flip vertical 0: close. 1: open. |
| Rotate | char | Range is {0, 1, 2, 3} 0: does not rotate. 1: 90° clockwise. 2: 180° clockwise. 3: 270° clockwise. 注：Range is {2} 此值是同时控制IE界面的这两个部件，IE上这两部件的组成的四种状态对应Rotate的0、1、2、3 |
| BackLightMode | char | Range is {0, 1} 0: disable. 1: enable. |
| BackLightLevel | char | Range is {0,1,2} 0: low 1: middle 2: high |
| R3dnrMode | char | Range is {0, 1, 2} 0: disable. 1: auto. 2: manual |
| R3dnrThreshTarget | unsigned char | Range is [0 ~ 0xff] thresh value when manual. |
| DISEnable | char | Range is {0, 1} 0: disable. 1: enable. 注：IPC不支持 |
| DefogMode | char | Range is {0, 1, 2} 0 : disable. 1: auto. 2: manual. |
| DefogStrength | char | Range is [0 ~ 100] Defog strength when used in manual mode. |
| DwdrMode | char | Range is {0, 1} 0: disable. 1: enable. |
| DwdrStrength | unsigned char | Range is [0 ~ 0xff] Drdw value when enabled DrdwMode. |
| GainControlMode | char | Range is {0, 1, 2, 3} 0: off. 1: low. 2: middle. 3: high |
| WBMode | char | Range is {0, 1, 2} 0: auto. 1: manual. 2: indoor. |
| Rgain | unsigned char | Range is [0 ~ 0xff]. |
| Ggain | unsigned char | Range is [0 ~ 0xff]. |
| Bgain | unsigned char | Range is [0 ~ 0xff]. |
| ShutterMode | char | Range is {0, 1}. 0: auto. 1: manual. |
| ShutterSpeed | char | Range is [0 ~ 30] ShutterUsecs value when manual. Max 1/25 in 50HZ, or max 1/30 in 60HZ. 注：IPC IE 实际上对应的Range is [0 ~ 26] |
| FlickerCtrl | char | Range is {0, 1, 2}. 0: 50HZ. 1: 60HZ. 2: disable. 注：因IPC私有协议不支持，该参数在此指令对应的接口中暂不支持设置，但能获取 |

9. 视频彩色参数

9.1参数获取请求格式：

POST /action/getConfig/VideoColor HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

9.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"Brightness":50,

"Contrast":50,

"Hue":50,

"Saturation":50,

"Sharpness":50

},

{

"channel":2,

"Brightness":50,

"Contrast":50,

"Hue":50,

"Saturation":50,

"Sharpness":50

}]

}

9.3参数设置请求格式：

POST /action/setConfig/VideoColor HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和9.2中参数获取回应的jason格式一致

}

9.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

9.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Color.Brightness | unsigned char | Brightness, range is [0 ~ 255] |
| Color.Contrast | unsigned char | Contrast, range is [0 ~ 255] |
| Color.Hue | unsigned char | Hue, range is [0 ~ 255] |
| Color.Saturation | unsigned char | Saturation, range is [0 ~ 255] |
| Color.Sharpness | unsigned char | Sharpness, range is [0 ~ 255] |

10. Live

10.1参数获取请求格式：

POST /action/getConfig/Live HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

10.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"ActionSwitch":1,

"StreamChoice":0

}

10.3参数设置请求格式：注：设置尚未实现

POST /action/setConfig/Live HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和10.2中参数获取回应的jason格式一致

}

10.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

10.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Live.ActionSwitch | char | Show record or alarm flag in preview window. 注：IPC不支持 |
| Live.StreamChoice | char | Preview stream. Range is {0, 1}. 0: main stream. 1: sub stream 注：IPC不支持 |

11. OSD

11.1参数获取请求格式：

POST /action/getConfig/OSDHTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

11.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"OsdNo":[{

"OsdNo":0

"OSDSwitch":1,

"OSDType":0,

"Alpha":50,

"Content":"raysharp-ipc",

"PosX":20,

"PosY":20

},

{

"OsdNo":1,

"OSDSwitch":1,

"OSDType":0,

"Alpha":50,

"Content":"raysharp-ipc",

"PosX":20,

"PosY":20

}]

},

{

"channel":2

"OsdNo":[{

"OsdNo":0

"OSDSwitch":1,

"OSDType":0,

"Alpha":50,

"Content":"raysharp-ipc",

"PosX":20,

"PosY":20

},

{

"OsdNo":1,

"OSDSwitch":1,

"OSDType":0,

"Alpha":50,

"Content":"raysharp-ipc",

"PosX":20,

"PosY":20

}]

}]

}

11.3参数设置请求格式：

POST /action/setConfig/OSD  HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和11.2中参数获取回应的jason格式一致

}

11.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

12.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Osd[OsdNo].OSDSwitch | char | Osd switch. 0: disable ; 1: enable. |
| Osd[OsdNo].OSDType | char | Osd type. 0: time; 1: name. |
| Osd[OsdNo].Alpha | unsigned char | Transparency of overlaid osd, the smaller the value, the more transparent it will be. Range is [0 ~ 128]. 注：IPC IE实际上对应为Range is [1 ~ 128]. |
| Osd[OsdNo].Content | string | Content of overlaid osd. Max length: 64. |
| Osd[OsdNo].PosX | integer | Osd postion. Top left x coordinate. |
| Osd[OsdNo].PosY | integer | Osd postion. Top left y coordinate. |

12. VideoCover

12.1参数获取请求格式：

POST /action/getConfig/VideoCover HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

12.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"Switch":1,

"CoReg":[{

"CoReg":0,

"Enable":1,

"Rect.X":10,

"Rect.Y":30,

"Rect.Width":100,

"Rect.Height":100

},

{

"CoReg":1,

"Enable":1,

"Rect.X":10,

"Rect.Y":30,

"Rect.Width":100,

"Rect.Height":100

}]

},

{

"channel":2,

"Switch":1,

"CoReg":[{

"CoReg":0,

"Switch":1,

"Enable":1,

"Rect.X":10,

"Rect.Y":30,

"Rect.Width":100,

"Rect.Height":100

},

{

"CoReg":1,

"Switch":1,

"Enable":1,

"Rect.X":10,

"Rect.Y":30,

"Rect.Width":100,

"Rect.Height":100

}]

}]

}

12.3参数设置请求格式：

POST /action/setConfig/VideoCover HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和12.2中参数获取回应的jason格式一致

}

12.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

12.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Cover.Switch | char | Video cover switch. 0: disable; 1: enable. |
| Cover[CoReg ].Enable | char | Each cover area switch. 0: disable; 1: enable. |
| Cover[CoReg ].Rect.X | integer | top left corner x coordinate (left) |
| Cover[CoReg ].Rect.Y | integer | top left corner y coordinate (top) |
| Cover[CoReg ].Rect.Width | integer | rect width. Range is [0 ~ 65535] 注：IPC IE实际上对应为rect width. Range is [0 ~ 576]. 此值不同的分辨率对应不同的max值，最大取值以分辨率对应的H,W为准 |
| Cover[CoReg ].Rect.Height | integer | rect width. Range is [0 ~ 65535] 注：IPC IE实际上对应为rect height. Range is [0 ~ 703]. 此值不同的分辨率对应不同的max值，最大取值以分辨率对应的H,W为准 |

13. ROI

13.1参数获取请求格式：

POST /action/getConfig/ROI HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13],

"StreamType" : 1  //0 -- mainstream; 1 -- substream; 2 -- mobilestream.

}

13.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

" channel":1,

" StreamType ":1, //0 -- mainstream; 1 -- substream; 2 -- mobilestream.

"RoiNo":[{

"RoiNo":0

"Index":5,

"Switch",1,

"IsAbsQp":1,

"Level":6,

"BgFrameRate":30,

"Rect.X":10,

"Rect.Y":30,

"Rect.Width":100,

"Rect.Height":100

},

{

"RoiNo":1

"Index":5,

"Switch",1,

"IsAbsQp":1,

"Level":6,

"BgFrameRate":30,

"Rect.X":10,

"Rect.Y":30,

"Rect.Width":100,

"Rect.Height":100

}]

},

{

" channel":2,

" StreamType ":1,

"RoiNo":[{

"RoiNo":0

"Index":5,

"Switch",1,

"IsAbsQp":1,

"Level":6,

"BgFrameRate":30,

"Rect.X":10,

"Rect.Y":30,

"Rect.Width":100,

"Rect.Height":100

},

{

"RoiNo":1

"Index":5,

"Switch",1,

"IsAbsQp":1,

"Level":6,

"BgFrameRate":30,

"Rect.X":10,

"Rect.Y":30,

"Rect.Width":100,

"Rect.Height":100

}]

}

}]

}

13.3参数设置请求格式：

POST /action/setConfig/ROI HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和13.2中参数获取回应的jason格式一致

}

13.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

13.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| ROI[RoiNo].Index | char | Range is [0 ~ 7]. Roi index, same as priority. The larger the index, the higher the priority. |
| ROI[RoiNo].Switch | char | 0: disable. 1: enable. |
| ROI[RoiNo].IsAbsQp | char | Range is {0, 1}. Whether to use absolute image quality. 0: relative quality. 1: absolute quality. 注：IPC不支持 |
| ROI[RoiNo].ILevel | char | Range is [1 ~ 6]. Roi value. The larger the value, the better the image quality. |
| ROI[RoiNo].BgFrameRate | char | Range is [0 ~ 30] Frame rate of non-ROI region. 注：IPC IE实际上对应为Range is [1 ~ 20] 不同分辨率对应不同帧率，以实际为准 |
| ROI[RoiNo].Rect.X | integer | Range is [0 ~ 65535]. top left corner x coordinate (left). 注：IPC IE实际上对应为Range is [0 ~ 704]. 此值最大值IPC私有协议中做了限定，以IE为准 |
| ROI[RoiNo].Rect.Y | integer | Range is [0 ~ 65535]. top left corner y coordinate (top). 注：IPC IE实际上对应为Range is [0 ~ 576]. 此值最大值IPC私有协议中做了限定，以IE为准 |
| ROI[RoiNo].Rect.Width | integer | rect width. |
| ROI[RoiNo].Rect.Height | integer | rect height. |

14. StreamUri

14.1参数获取请求格式：

POST /action/getConfig/StreamUri HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"Channel": [{

"channel": 0,

"StreamType": 0

},

{

"channel": 1,

"StreamType": 1

}]

}

14.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"StreamUrl":"rtsp://192.168.6.67:554/ch01/0",

},

{

"StreamUrl":"rtsp://192.168.6.67:554/ch02/1"

}]

}

14.3 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Channel | unsigned integer | Channel |
| StreamType | char | Range is {0, 1,2}. 0: main stream. 1: sub stream. 2:mobile stream.. |

- MainStream

15.1参数获取请求格式：

POST /action/getConfig/MainStream HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

15.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"VideoType":0,

"BitrateType":0,

"BitrateMode":0,

"Fps":25,

"CustomBitrate":4096,

"Bitrate":3,

"Resolution":1,

"VideoQuality":4,

"IFrameInterval":30,

"LoadBalancing":0,

"AudioSwitch":1,

"ProfileLevel":1

},

{

"channel":2,

"VideoType":0,

"BitrateType":0,

"BitrateMode":0,

"Fps":25,

"CustomBitrate":4096,

"Bitrate":3,

"Resolution":1,

"VideoQuality":4,

"IFrameInterval":30,

"LoadBalancing":0,

"AudioSwitch":1,

"ProfileLevel":1

}]

}

15.3参数设置请求格式：

POST /action/setConfig/MainStream HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和16.2中参数获取回应的jason格式一致

}

15.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

15.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| MainStream.VideoType | char | Range is {0, 1}. Video rate type. 0: H.264. 1: H.265. |
| MainStream.BitrateType | char | Range is {0, 1, 2}. 注：IPC IE实际上对应为Range is {0, 1} 0: CBR. 1: VBR. 2. FIX QP |
| MainStream.BitrateMode | char | Range is {0, 1}. Rate mode. 0: pre define. 1: self define. |
| MainStream.Fps | char | Range is [1 ~ 25 ]. PAL; or [1 ~ 30] NTSC. Frames per second. |
| MainStream.CustomBitrate | unsigned integer | Range is [1 ~ 16M]. Bitrate value that user can choose. |
| MainStream.Resolution | char | Range {0, 1, 2, 3, 4, 5}. 0: 300W. 1: 1080P. 2: 960P. 3: 720P. 4: VGA. 5: QVGA. |
| MainStream.VideoQuality | char | Range {0, 1, 2, 3, 4, 5}. 0: worst. 1: worse. 2: pool. 3: good. 4: better. 5: best. |
| MainStream.IFrameInterval | char | Range is [1 ~ 100]. unit is second. I Frame interval. |
| MainStream.LoadBalancing | char | Range is {0, 1}. Load balance. 0: real time 1: balanced. 注：IPC不支持 |
| MainStream.AudioSwitch | char | Audio switch. 0: off. 1: on. |
| ProfileLevel | char | Range is {0, 1, 2}. Profile level. 0: Baseline. 1: Main Profile. 2: High Profile. |

16. SubStream

16.1参数获取请求格式：

POST /action/getConfig/SubStream  HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

16.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"VideoType":0,

"BitrateType":0,

"BitrateMode":0,

"Fps":15,

"CustomBitrate":2048,

"Bitrate":3,

"Resolution":1,

"VideoQuality":4,

"IFrameInterval":30,

"LoadBalancing":0,

"AudioSwitch":1,

"ProfileLevel":1

},

{

"channel":2,

"VideoType":0,

"BitrateType":0,

"BitrateMode":0,

"Fps":15,

"CustomBitrate":2048,

"Bitrate":3,

"Resolution":1,

"VideoQuality":4,

"IFrameInterval":30,

"LoadBalancing":0,

"AudioSwitch":1,

"ProfileLevel":1

}]

}

16.3参数设置请求格式：

POST /action/setConfig/SubStream HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和16.2中参数获取回应的jason格式一致

}

16.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

16.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| SubStream.VideoType | char | Range is {0, 1}. Video rate type. 0: H.264. 1: H.265. |
| SubStream.BitrateType | char | Range is {0, 1, 2}. 注：IPC IE实际上对应为Range is {0, 1} 0: CBR. 1: VBR. 2. FIX QP |
| SubStream.BitrateMode | char | Range is {0, 1}. Rate mode. 0: pre define. 1: self define. |
| SubStream.Fps | char | Range is [1 ~ 25 ]. PAL; or [1 ~ 30] . NTSC. Frames per second. |
| SubStream.CustomBitrate | unsigned integer | Range is [1 ~ 16M]. Bitrate value that user can choose. |
| SubStream.Resolution | char | Range {0, 1, 2, 3, 4, 5}.注：IPC IE实际上对应为Range is {0, 1, 2} 0: 300W. 1: 1080P. 2: 960P. 3: 720P. 4: VGA. 5: QVGA. |
| SubStream.VideoQuality | char | Range {0, 1, 2, 3, 4, 5}. 0: worst. 1: worse. 2: pool. 3: good. 4: better. 5: best. |
| SubStream.IFrameInterval | char | Range is [1 ~ 100]. unit is second. I Frame interval. |
| SubStream.LoadBalancing | char | Range is {0, 1}. Load balance. 0: real time 1: balanced. 注：IPC不支持 |
| SubStream.AudioSwitch | char | Audio switch. 0: off. 1: on. |
| SubStream.ProfileLevel | char | Range is {0, 1, 2}. Profile level. 0: Baseline. 1: Main Profile. 2: High Profile. |

17. MobileStream

17.1参数获取请求格式：

POST /action/getConfig/MobileStream HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

17.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"VideoSwitch":1,

"VideoType":0,

"BitrateType":0,

"BitrateMode":0,

"Fps":10,

"CustomBitrate":512,

"Bitrate":3,

"Resolution":1,

"VideoQuality":4,

"IFrameInterval":30,

"LoadBalancing":0,

"AudioSwitch":1,

"ProfileLevel":1

},

{

"channel":2,

"VideoSwitch":1,

"VideoType":0,

"BitrateType":0,

"BitrateMode":0,

"Fps":10,

"CustomBitrate":512,

"Bitrate":3,

"Resolution":1,

"VideoQuality":4,

"IFrameInterval":30,

"LoadBalancing":0,

"AudioSwitch":1,

"ProfileLevel":1

}]

}

17.3参数设置请求格式：

POST /action/setConfig/MobileStream HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和17.2中参数获取回应的jason格式一致

}

17.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

17.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| MobileStream.VideoSwitch | char | Video switch. 0: disabled. 1: enabled. |
| MobileStream.VideoType | char | Range is {0, 1}. Video rate type. 0: H.264. 1: H.265. |
| MobileStream.BitrateType | char | Range is {0, 1, 2}. 注：IPC IE实际上对应为Range is {0, 1} 0: CBR. 1: VBR. 2. FIX QP |
| MobileStream.BitrateMode | char | Range is {0, 1}. Rate mode. 0: pre define. 1: self define. |
| MobileStream.Fps | char | Range is [1 ~ 25 ]. PAL; or [1 ~ 30] . NTSC. Frames per second. |
| MobileStream.CustomBitrate | unsigned integer | Range is [1 ~ 16M]. Bitrate value that user can choose. |
| MobileStream.Resolution | char | Range {0, 1, 2, 3, 4, 5}.注：IPC IE实际上对应为Range is {0, 1} 0: 300W. 1: 1080P. 2: 960P. 3: 720P. 4: VGA. 5: QVGA. |
| MobileStream.VideoQuality | char | Range {0, 1, 2, 3, 4, 5}. 0: worst. 1: worse. 2: pool. 3: good. 4: better. 5: best. |
| MobileStream.IFrameInterval | char | Range is [1 ~ 100]. unit is second. I Frame interval. |
| MobileStream.LoadBalancing | char | Range is {0, 1}. Load balance. 0: real time 1: balanced. 注：IPC不支持 |
| MobileStream.AudioSwitch | char | Audio switch. 0: off. 1: on. |
| MobileStream.ProfileLevel | char | Range is {0, 1, 2}. Profile level. 0: Baseline. 1: Main Profile. 2: High Profile. |

18. Audio

18.1参数获取请求格式：

POST /action/getSysConfig/Audio HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

18.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"Switch":1,

"MicInVolume":5,

"LineOutVolume":6,

"Type":0,

"Bitrate":0

},

{

"channel":2,

"Switch":1,

"MicInVolume":5,

"LineOutVolume":6,

"Type":0,

"Bitrate":0

}]

}

18.3参数设置请求格式：

POST /action/setSysConfig/Audio HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和18.2中参数获取回应的jason格式一致

}

18.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

18.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Audio.Switch | unsigned char | Audio switch. 0: off. 1: on. |
| Audio.Type | char | Range is {0, 1, 2, 3}. Audio type. 0: G711A; 1: G711U. 2: G726; 3: ADPCM. |
| Audio.Bitrate | unsigned char | Current set to 0 which means 64k. 注：IPC不支持 |
| Audio.MicInVolume | unsigned char | Range is [0 ~ 10]. In volume value. |
| Audio.LineOutVolume | unsigned char | Range is [0 ~ 10]. Out volume value. |

19.NetWork

19.1参数获取请求格式：

POST /action/getNetConfig/NetBase HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

19.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"IPAddress":192.168.1.240,

"Netmask":255.255.255.0,

"Gateway":192.168.1.1,

"Dns1":8.8.8.8,

"Dns2":221.96.128.86,

"PPPOEuser":"raysharp",

"Password":"519070",

"NetworkMode":2,

"ClientPort":9001,

"WebPort":80,

"MobilePort":18040,

"UseUPNP":0

}

19.3参数设置请求格式：

POST /action/setNetConfig/NetBase HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和19.2中参数获取回应的jason格式一致

}

19.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

19.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| NetBase.IPAddress | string | Interface IP address. Max length: 32. |
| NetBase.Netmask | string | Network mask string: In the form of x.x.x.x, range of x is [0-255] Example: 255.255.255.0 |
| NetBase.Gateway | string | Gateway address. |
| NetBase.Dns1 | string | IP address of first DNS server. |
| NetBase.Dns2 | string | IP address of second DNS server. |
| NetBase.PPPOEuser | string | PPPoE User name. Max length: 32. |
| NetBase.Password | string | PPPoE User password. Max length: 32. |
| NetBase.NetworkMode | char | Range is {0, 1, 2}. Networking mode. 0: DHCP. 1: PPPOE. 2: manual. |
| NetBase.ClientPort | unsigned short | Client port. |
| NetBase.WebPort | unsigned short | Web port. |
| NetBase.MobilePort | unsigned short | Mobile port. |
| NetBase.UseUPNP | char | Enable / disable UPnP. 0: disable. 1: enable. |

20.DDNS

20.1参数获取请求格式:

POST /action/getNetConfig/DDNS HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

20.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"HostName":    "raysharp"

"ServerAddr":    "anlian.co"，

"UserName":    "raysharp"，

"Password":     "519070"，

"UseFlag":     1，

"Switch":1，

"UpdateInterval":3

}

20.3参数设置请求格式：

POST /action/setNetConfig/DDNS HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和20.2中参数获取回应的jason格式一致

}

20.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

20.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| DDNS.HostName | string | Host name of this device. Max length: 32. |
| DDNS.ServerAddr | string | DDNS server IP address or name. Max length: 32. |
| DDNS.UserName | string | DDNS user name. Max length: 32. |
| DDNS.Password | string | DDNS user password. Max length: 32. |
| DDNS.UseFlag | unsigned integer | DDNS use flag. Each bit correspond to a type of DDNS. |
| DDNS.Switch | unsigned char | DDSN switch. 0: disable. 1: enable. |
| DDNS.UpdateInterval | unsigned char | Range is [0 ~ 255]. DDNS update interval. 注：IPC不支持 |

21.Email

21.1参数获取请求格式:

POST /action/getNetConfig/Email HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

21.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Address":      "www.163.com"，

"Sender":       "www.raysharp.cn"，

"Password":     123456，

"Receivers_1":   "x@raysharp.cn",

"Receivers_2":   "y@raysharp.cn",

"Receivers_3":   "z@raysharp.cn",

"Port":        26，

"SSLSwitch":   1,

"EmailSwitch":   1,

"Intervaltime":   180

}

21.3参数设置请求格式：

POST /action/setNetConfig/Email HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和21.2中参数获取回应的jason格式一致

}

21.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

21.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Email.Address | string | SMTP server IP address or name. Max length: 32. |
| Email.Sender | string | Sender address. Max length: 32. |
| Email.Password | string | Sender password. Max length: 32. |
| Email.Receivers[0] | string | Email addresses of 3 receivers. Max length: 32. |
| Email.Receivers[1] |  |  |
| Email.Receivers[2] |  |  |
| Email.Port | unsigned short | Range is [1-65535]. |
| Email.SSLSwitch | char | 1: enable SSL email. |
| Email.EmailSwitch | char | 0: disable. 1: enable email. |
| Email.Intervaltime | short | Range is {180, 300, 600}. unit is second. |

22.P2P

23.1参数获取请求格式:

POST /action/getNetConfig/P2P HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

22.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Uid":         "rs123456"，

"UserName":   "raysharp"，

"Password":    "519070"，

"State":        1

}

22.3参数设置请求格式：

POST /action/setNetConfig/P2P HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和22.2中参数获取回应的jason格式一致

}

22.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

22.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| P2P.Uid | string | P2P id. Max length: 32. |
| P2P.UserName | string | P2P user name. Max length: 32. 注：IPC不支持 |
| P2P.Password | string | P2P user password. Max length: 32. 注：IPC不支持 |
| P2P.State | char | P2P connect status. 注：IPC不支持 |

23.RTSP

23.1参数获取请求格式

POST /action/getNetConfig/RTSP HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

23.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"UserName":        "raysharp"，

"Password":         "519070"，

"Port":              554，

"CheckFlag":        1,

"Switch":          1,

"AuthType":       1

}

23.3参数设置请求格式：

POST /action/setNetConfig/RTSP HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和23.2中参数获取回应的jason格式一致

}

23.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

23.5 参数说明：

| URL Syntax | http://<ip>/action/getNetConfig?name=RTSP |
| --- | --- |
| Comment |  |
| Response | RTSP.UserName=raysharp RTSP.Password=519070 RTSP.Port=554 RTSP.CheckFlag=1 RTSP.Switch=1 RTSP.AuthType=1 |

24. FTP

24.1参数获取请求格式

POST /action/getNetConfig/FTP HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

24.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"IPAddress":        "192.168.1.120"，

"UserName":        "anonymity"，

"Password":         "123456"，

"Port":              21,

"Switch":          1,

"TimeInterval":     3,

"ReqTypeMask":    2,

"RecType":         1,

"FilePath":          "share"

}

24.3参数设置请求格式：

POST /action/setNetConfig/FTP HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和24.2中参数获取回应的jason格式一致

}

24.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

24.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| FTP.IPAddress | string | FTP IP address. Max length: 32. |
| FTP.UserName | string | Login user name. Max length: 32. |
| FTP.Password | string | Login user password. Max length: 32. |
| FTP.Port | integer | FTP port. |
| FTP.Switch | char | 0: off. 1: on. |
| FTP.TimeInterval | char | Range is [0 ~ 128]. Period of time to upload video. |
| FTP.ReqTypeMask | char | Req type mask .Bitwise representation. 0 bit: close. 2bit: image. 3bit: video |
| FTP.RecType | char | Range is {1, 2, 3}. 1: normal record. 2: alarm record. 3: all record. |
| FTP.FilePath | string | FTP file path. Max length: 96. Directory name. |

25. IOAlarm

25.1参数获取请求格式：

POST /action/getAlarmConfig/IOAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

25.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"AlarmSet":              1，

"AlarmOutTime":         10，

"RecordDelayTime":      30，

"AlarmOutManager":      1,

"EmailLink":            0,

"RecordSwitch":        1,

"FtpUploadSwitch":      0,

"CloudSwitch":          0,

"PushSwitch":          0

},

{

"channel":2,

"AlarmSet":              1，

"AlarmOutTime":         10，

"RecordDelayTime":      30，

"AlarmOutManager":      1,

"EmailLink":            0,

"RecordSwitch":        1,

"FtpUploadSwitch":      0,

"CloudSwitch":          0,

"PushSwitch":          0

}]

}

25.3参数设置请求格式：

POST /action/setAlarmConfig/IOAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和26.2中参数获取回应的jason格式一致

}

25.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

25.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| IOAlarm.AlarmSet | char | Range is {0, 1, 2}. IO status alarm. 0: normal open. 1: normal close. 2: closed. |
| IOAlarm.AlarmOutTime | char | Range is 10, 20, 40, 60, 30s, 1min , 2min. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| IOAlarm.RecordDelayTime | char | Range is 10, 30, 1min, 2min, 5mins. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| IOAlarm.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| IOAlarm.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| IOAlarm.RecordSwitch | char | 0: disable. 1: enable. |
| IOAlarm.FtpUploadSwitch | char | 0: disable. 1: enable. |
| IOAlarm.CloudSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| IOAlarm.PushSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |

26. Motion

26.1参数获取请求格式：

POST /action/getAlarmConfig/Motion HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

26.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"Switch":              1，

"Sensitivity":            4,

"AlarmOutTime":         10，

"RecordDelayTime":      30，

"AlarmOutManager":      1,

"EmailLink":            0,

"RecordSwitch":        1,

"FtpUploadSwitch":      0,

"CloudSwitch":          0,

"PushSwitch":          0

"Region_0":			"03-CD-5E-7F-12-6A-49-FB-6C-10-2D"

// ......

"Region_17":			"4B-AF-71-CE-38-90-A6-CA-DF-33-5C"

},

{

"channel":2,

"Switch":              1，

"Sensitivity":            4,

"RecordDelayTime":      20，

"AlarmOutManager":      1,

"EmailLink":            1,

"RecordSwitch":         0,

"FtpUploadSwitch":      0,

"CloudSwitch":          1,

"PushSwitch":          0

"Region_0":			"03-CD-5E-7F-12-6A-49-FB-6C-10-2D"

// ......

"Region_17":			"4B-AF-71-CE-38-90-A6-CA-DF-33-5C"

}

// ......

}

26.3参数设置请求格式：

POST /action/setAlarmConfig/Motion HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和26.2中参数获取回应的jason格式一致

}

26.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

26.5 参数说明:

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Motion.Switch | char | Enable/Disable motion detect feature in a channel. |
| Motion.Sensitivity | char | Range is [1-8]. Sensitivity of motion detection. 1: lowest sensitivity. 8: highest sensitivity. 注：实际上Range is [0-7]. Sensitivity of motion detection. 0: lowest sensitivity. 7: highest sensitivity. |
| Motion.Region[LineNum] | integer | Currently, region is divided into 36 lines and 44 blocks/line. A bit describes a block in the line. Bit = 1: motion in this block is monitored.. Example: Region[0] = (FF-FF-FF-FF-FF-F0-00-00-00-00-00):: motion in channel 0 line 0’s 44 blocks is monitored. Line 1’s 44 blocks not monitored. |
| Motion.AlarmOutTime | char | Range is 10, 20, 40, 60, 30s, 1min , 2min. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| Motion.RecordDelayTime | char | Range is 10, 30, 1min, 2min, 5mins. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| Motion.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| Motion.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| Motion.RecordSwitch | char | 0: disable. 1: enable. |
| Motion.FtpUploadSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| Motion.CloudSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| Motion.PushSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |

27. PerimLine

27.1参数获取请求格式：

POST /action/getAlarmConfig/PerimLine HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

27.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel": [{

"channel":1,

"ChnSwitch":0,

"AlarmOutTime":10,

"RecordDelayTime":20,

"AlarmOutManager": 1,

"EmailLink": 0,

"RecordSwitch": 1,

"FtpUploadSwitch" : 0,

"CloudSwitch" : 0,

"PushSwitch" : 0,

"RuleSwitch": 1,

"RuleType": 1,

"LineTwoWay": 1,

"Scene" : 1,

"Sensitive" : 3,

"LineNo" : 2,

"RuleLine": [{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

},

{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

}]

},

{

"channel":3,

"ChnSwitch":1,

"AlarmOutTime":20,

"RecordDelayTime":40,

"AlarmOutManager": 1,

"EmailLink": 1,

"RecordSwitch": 1,

"FtpUploadSwitch" : 1,

"CloudSwitch" : 1,

"PushSwitch" : 1,

"RuleSwitch": 0,

"RuleType": 0,

"LineTwoWay": 0,

"Scene" : 0,

"Sensitive" : 2,

"LineNo" : 2,

"RuleLine": [{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

},

{

""StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

}]

}]

}

27.3参数设置请求格式：

POST /action/setAlarmConfig/PerimLine HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和27.2中参数获取回应的jason格式一致

}

27.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

27.5 参数说明:

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| PerimLine.ChnSwitch | char | 0: close. 1: open. |
| PerimLine.AlarmOutTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| PerimLine.RecordDelayTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| PerimLine.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| PerimLine.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| PerimLine.RecordSwitch | char | 0: disable. 1: enable. |
| PerimLine.FtpUploadSwitch | char | 0: disable. 1: enable. |
| PerimLine.CloudSwitch | char | 0: disable. 1: enable. |
| PerimLine.PushSwitch | char | 0: disable. 1: enable. |
| PerimLine.RuleSwitch | char | Each channel use one byte to represent at most 4 rules. 0 - close; 1 - in use. |
| PerimLine.RuleType | char | Each channel use one byte to represent at most 4 rules type. 0 - satellite line; 1 - perimeter line. |
| PerimLine.LineTwoWay | char | Each channel use one byte to represent at most 4 satellite type. 0 - not two way; 1 - two way. 注：IPC不支持 |
| PerimLine.Scene | char | Scene. 0: indoor, 1: outdoor. |
| PerimLine.Sensitive | char | Sensitive. Range is {0, 1, 2, 3}. |
| PerimLine.RuleLine[LineNo ].StartX | short | Start x coordinate of perimeter line. |
| PerimLine.RuleLine[LineNo ].StartY | short | Start y coordinate of perimeter line. |
| PerimLine.RuleLine[LineNo ].EndX | short | End x coordinate of perimeter line. |
| PerimLine.RuleLine[LineNo ].EndY | short | End y coordinate of perimeter line. |

28. Perimeter

28.1参数获取请求格式：

POST /action/getAlarmConfig/Perimeter HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

28.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel": [{

"channel":1,

"ChnSwitch":0,

"AlarmOutTime":10,

"RecordDelayTime":20,

"AlarmOutManager": 1,

"EmailLink": 0,

"RecordSwitch": 1,

"FtpUploadSwitch" : 0,

"CloudSwitch" : 0,

"PushSwitch" : 0,

"RuleSwitch": 1,

"RuleType": 1,

"LineTwoWay": 1,

"Scene" : 1,

"Sensitive" : 3,

"LineNo" : 2,

"RuleLine": [{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

},

{

"LineNo" : 2,

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

}]

},

{

"channel":3,

"ChnSwitch":1,

"AlarmOutTime":20,

"RecordDelayTime":40,

"AlarmOutManager": 1,

"EmailLink": 1,

"RecordSwitch": 1,

"FtpUploadSwitch" : 1,

"CloudSwitch" : 1,

"PushSwitch" : 1,

"RuleSwitch": 0,

"RuleType": 0,

"LineTwoWay": 0,

"Scene" : 0,

"Sensitive" : 2,

"LineNo" : 2,

"RuleLine": [{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

},

{

"LineNo" : 5,

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

}]

}]

}

28.3参数设置请求格式：

POST /action/setAlarmConfig/Perimeter HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和28.2中参数获取回应的jason格式一致

}

28.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

28.5 参数说明:

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Perimeter ChnSwitch | char | 0: close. 1: open. |
| Perimeter.AlarmOutTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| Perimeter.RecordDelayTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| Perimeter.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| Perimeter.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| Perimeter.RecordSwitch | char | 0: disable. 1: enable. |
| Perimeter.FtpUploadSwitch | char | 0: disable. 1: enable. |
| Perimeter.CloudSwitch | char | 0: disable. 1: enable. |
| Perimeter PushSwitch | char | 0: disable. 1: enable. |
| Perimeter.RuleSwitch | char | Each channel use one byte to represent at most 4 rules. 0 - close; 1 - in use. |
| Perimeter.RuleType | char | Each channel use one byte to represent at most 4 rules type. 0 - satellite line; 1 - perimeter line. |
| Perimeter.LineTwoWay | char | Each channel use one byte to represent at most 4 satellite type. 0 - not two way; 1 - two way. |
| Perimeter.Scene | char | Scene. 0: indoor, 1: outdoor. |
| Perimeter.Sensitive | char | Sensitive. Range is {0, 1, 2, 3}. |
| Perimeter RuleLine[LineNo ].StartX | short | Start x coordinate of perimeter line. |
| Perimeter.RuleLine[LineNo ].StartY | short | Start y coordinate of perimeter line. |
| Perimeter.RuleLine[LineNo ].EndX | short | End x coordinate of perimeter line. |
| Perimeter.RuleLine[LineNo ].EndY | short | End y coordinate of perimeter line. |

29. SODAlarm

29.1参数获取请求格式：

POST /action/getAlarmConfig/SODAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

29.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel" :   [{

"channel":1,

"ChnSwitch": 1,

"AlarmOutTime": 10,

"RecordDelayTime": 10,

"AlarmOutManager": 1,

"EmailLink": 0,

"RecordSwitch": 1,

"FtpUploadSwitch": 0,

"CloudSwitch": 0,

"PushSwitch": 0,

"RuleSwitch":1,

"RuleType":1,

"RuleRectEnable": [1,1,1,1],

"Scene": 1,

"Sensitive": 2,

"RectNo":2,

"Rect":[ {

"X": 10,

"Y": 10,

"Width": 50,

"Height":50

},

{

"X": 10,

"Y": 10,

"Width": 50,

"Height":50

}]

},

{

"channel":2,

"ChnSwitch": 0,

"AlarmOutTime": 20,

"RecordDelayTime": 20,

"AlarmOutManager": 1,

"EmailLink": 1,

"RecordSwitch": 0,

"FtpUploadSwitch": 1,

"CloudSwitch": 1,

"PushSwitch": 1,

"RuleSwitch":0,

"RuleType":0,

"RuleRectEnable": [1,1,1,1],

"Scene": 0,

"Sensitive": 1,

"RectNo":2,

"Rect":[{

"X": 10,

"Y": 10,

"Width": 50,

"Height":50

},

{

"X": 10,

"Y": 10,

"Width": 50,

"Height":50

}]

}]

}

29.3参数设置请求格式：

POST /action/setAlarmConfig/SODAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和29.2中参数获取回应的jason格式一致

}

29.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

29.5 参数说明:

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| SODAlarm.ChnSwitch | char | 0: close. 1: open. |
| SODAlarm.AlarmOutTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| SODAlarm.RecordDelayTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| SODAlarm.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| SODAlarm.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| SODAlarm.RecordSwitch | char | 0: disable. 1: enable. |
| SODAlarm.FtpUploadSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| SODAlarm.CloudSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| SODAlarm.PushSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| SODAlarm.RuleSwitch | char | Each channel use one byte to represent at most 4 rules. 0 - close; 1 - in use. |
| SODAlarm.RuleType | char | Each channel use one byte to represent at most 4 rules type. 0 - left; 1 - lost. |
| SODAlarm.RuleRectEnable[0] | char | Each channel has at most 4 rules, each rule has at most 4 regions, each bit represent a status of a region. 0 - disable; 1 - enable. |
| SODAlarm.RuleRectEnable[1] |  |  |
| SODAlarm.RuleRectEnable[2] |  |  |
| SODAlarm.RuleRectEnable[3] |  |  |
| SODAlarm.Scene | char | Scene. 0: indoor, 1: outdoor. |
| SODAlarm.Sensitive | char | Sensitive. Range is {0, 1, 2, 3}. |
| SODAlarm.RuleLine[LineNo ].StartX | short | Start x coordinate of rule line. |
| SODAlarm.RuleLine[LineNo ].StartY | short | Start y coordinate of rule line.. |
| SODAlarm. .RuleLine[LineNo ].EnX | short | End x coordinate of rule line.. |
| SODAlarm. .RuleLine[LineNo ].EnY | short | End y coordinate of rule line. |

30. PDAlarm

30.1参数获取请求格式：

POST /action/getAlarmConfig/PDAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

30.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel": [{

"channel":1,

"ChnSwitch":0,

"AlarmOutTime":10,

"RecordDelayTime":20,

"AlarmOutManager": 1,

"EmailLink": 0,

"RecordSwitch": 1,

"FtpUploadSwitch" : 0,

"CloudSwitch" : 0,

"PushSwitch" : 0,

"RuleSwitch": 1,

"RuleType": 1,

"Scene" : 1,

"Sensitive" : 3,

"LineNo" : 2,

"RuleLine": [{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

},

{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

}]

},

{

"channel":3,

"ChnSwitch":1,

"AlarmOutTime":20,

"RecordDelayTime":40,

"AlarmOutManager": 1,

"EmailLink": 1,

"RecordSwitch": 1,

"FtpUploadSwitch" : 1,

"CloudSwitch" : 1,

"PushSwitch" : 1,

"RuleSwitch": 0,

"RuleType": 0,

"Scene" : 0,

"Sensitive" : 2,

"LineNo" : 2,

"RuleLine": [{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

},

{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

}]

}]

}

30.3参数设置请求格式：

POST /action/setAlarmConfig/PDAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和30.2中参数获取回应的jason格式一致

}

30.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

30.5 参数说明:

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| PD Alarm.ChnSwitch | char | 0: close. 1: open. |
| PDAlarm.AlarmOutTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| PDAlarm.RecordDelayTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| PDAlarm.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| PDAlarm.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| PDAlarm.RecordSwitch | char | 0: disable. 1: enable. |
| PDAlarm FtpUploadSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| PDAlarm.CloudSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| PDarm.PushSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| PDAlarm.RuleSwitch | char | Each channel use one byte to represent at most 4 rules. 0 - close; 1 - in use. |
| PDAlarm.RuleType | char | Each channel use one byte to represent at most 4 rules type. 0 - general mode; 1 - visit mode. |
| PDAlarm.Scene | char | Scene. 0: indoor, 1: outdoor. |
| PDAlarm.Sensitive | char | Sensitive. Range is {0, 1, 2, 3}. |
| PDAlarm.RuleLine[LineNo ].StartX | short | Start x coordinate of rule line. |
| PDAlarm.RuleLine[LineNo ].StartY | short | Start y coordinate of rule line. |
| PDAlarm.RuleLine[LineNo ].EndX | short | End x coordinate of rule line. |
| PDAlarm.RuleLine[LineNo ].EndY | short | End y coordinate of rule line. |

31. FDAlarm

31.1参数获取请求格式：

POST /action/getAlarmConfig/FDAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

31.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel": [{

"channel":1,

"ChnSwitch":0,

"AlarmOutTime":10,

"RecordDelayTime":20,

"AlarmOutManager": 1,

"EmailLink": 0,

"RecordSwitch": 1,

"FtpUploadSwitch" : 0,

"CloudSwitch" : 0,

"PushSwitch" : 0,

"RuleSwitch": 1,

"RuleType": 1,

"Scene" : 1,

"Sensitive" : 3,

"LineNo" : 2,

"RuleLine": [{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

},

{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

}]

},

{

"channel":3,

"ChnSwitch":1,

"AlarmOutTime":20,

"RecordDelayTime":40,

"AlarmOutManager": 1,

"EmailLink": 1,

"RecordSwitch": 1,

"FtpUploadSwitch" : 1,

"CloudSwitch" : 1,

"PushSwitch" : 1,

"RuleSwitch": 0,

"RuleType": 0,

"Scene" : 0,

"Sensitive" : 2,

"LineNo" : 2,

"RuleLine": [{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

},

{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

}]

}]

}

31.3参数设置请求格式：

POST /action/setAlarmConfig/FDAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和31.2中参数获取回应的jason格式一致

}

31.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

31.5 参数说明:

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| PD Alarm.ChnSwitch | char | 0: close. 1: open. |
| PDAlarm.AlarmOutTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| PDAlarm.RecordDelayTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| PDAlarm.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| PDAlarm.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| PDAlarm.RecordSwitch | char | 0: disable. 1: enable. |
| PDAlarm FtpUploadSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| PDAlarm.CloudSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| PDarm.PushSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| PDAlarm.RuleSwitch | char | Each channel use one byte to represent at most 4 rules. 0 - close; 1 - in use. |
| PDAlarm.RuleType | char | Each channel use one byte to represent at most 4 rules type. 0 - general mode; 1 - visit mode. |
| PDAlarm.Scene | char | Scene. 0: indoor, 1: outdoor. |
| PDAlarm.Sensitive | char | Sensitive. Range is {0, 1, 2, 3}. |
| PDAlarm.RuleLine[LineNo ].StartX | short | Start x coordinate of rule line. |
| PDAlarm.RuleLine[LineNo ].StartY | short | Start y coordinate of rule line. |
| PDAlarm.RuleLine[LineNo ].EndX | short | End x coordinate of rule line. |
| PDAlarm.RuleLine[LineNo ].EndY | short | End y coordinate of rule line. |

32. CCAlarm

32.1参数获取请求格式：

POST /action/getAlarmConfig/CCAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

32.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel": [{

"channel":1,

"ChnSwitch":0,

"AlarmOutTime":10,

"RecordDelayTime":20,

"AlarmOutManager": 1,

"EmailLink": 0,

"RecordSwitch": 1,

"FtpUploadSwitch" : 0,

"CloudSwitch" : 0,

"PushSwitch" : 0,

"RuleSwitch": 1,

"RuleType": 1,

"Scene" : 1,

"Sensitive" : 3,

"LineNo" : 2,

"RuleLine": [{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

},

{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

}]

},

{

"channel":3,

"ChnSwitch":1,

"AlarmOutTime":20,

"RecordDelayTime":40,

"AlarmOutManager": 1,

"EmailLink": 1,

"RecordSwitch": 1,

"FtpUploadSwitch" : 1,

"CloudSwitch" : 1,

"PushSwitch" : 1,

"RuleSwitch": 0,

"RuleType": 0,

"Scene" : 0,

"Sensitive" : 2,

"LineNo" : 2,

"RuleLine": [{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

},

{

"StartX" : 10,

"StartY" : 10,

"EndX" : 20,

"EndY" : 30

}]

}]

}

32.3参数设置请求格式：

POST /action/setAlarmConfig/CCAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和32.2中参数获取回应的jason格式一致

}

32.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

32.5 参数说明:

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| PD Alarm.ChnSwitch | char | 0: close. 1: open. |
| PDAlarm.AlarmOutTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| PDAlarm.RecordDelayTime | char | Range is {0, 1, 2, 3, 4}. Successively represent : 0, 10, 20, 40, 60. 注：IPC IE实际上Range is {0,1,2,3} 即5 10 20 30s |
| PDAlarm.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| PDAlarm.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| PDAlarm.RecordSwitch | char | 0: disable. 1: enable. |
| PDAlarm FtpUploadSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| PDAlarm.CloudSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| PDarm.PushSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| PDAlarm.RuleSwitch | char | Each channel use one byte to represent at most 4 rules. 0 - close; 1 - in use. |
| PDAlarm.RuleType | char | Each channel use one byte to represent at most 4 rules type. 0 - general mode; 1 - visit mode. |
| PDAlarm.Scene | char | Scene. 0: indoor, 1: outdoor. |
| PDAlarm.Sensitive | char | Sensitive. Range is {0, 1, 2, 3}. |
| PDAlarm.RuleLine[LineNo ].StartX | short | Start x coordinate of rule line. |
| PDAlarm.RuleLine[LineNo ].StartY | short | Start y coordinate of rule line. |
| PDAlarm.RuleLine[LineNo ].EndX | short | End x coordinate of rule line. |
| PDAlarm.RuleLine[LineNo ].EndY | short | End y coordinate of rule line. |

33. ODAlarm

33.1参数获取请求格式：

POST /action/getAlarmConfig/ODAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

33.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"Channel":1,

"Switch" : 1 ,

"Sensitivity" : 3,

"AlarmOutTime": 10 ,

"RecordDelayTime" : 30 ,

"AlarmOutManager" : 1,

"EmailLink" : 0,

"RecordSwitch" : 1 ,

"FtpUploadSwitch" : 0 ,

"CloudSwitch" : 0 ,

"PushSwitch" : 0

},

{

"Channel":2,

"Switch" : 1 ,

"Sensitivity" : 3,

"AlarmOutTime": 10 ,

"RecordDelayTime" : 30 ,

"AlarmOutManager" : 1,

"EmailLink" : 0,

"RecordSwitch" : 1 ,

"FtpUploadSwitch" : 0 ,

"CloudSwitch" : 0 ,

"PushSwitch" : 0

}]

}

33.3参数设置请求格式：

POST /action/setAlarmConfig/ODAlarm HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和33.2中参数获取回应的jason格式一致

}

33.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

33.5 参数说明:

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| ODAlarm.Switch | char | 0: disable. 1: enable. |
| ODAlarm.Sensitivity | char | Range is [1 ~ 6]. Sensitivity of OD. 1: lowest sensitivity. 6: highest sensitivity. 注：实际上Range is [0 ~ 5]. Sensitivity of OD. 0: lowest sensitivity. 5: highest sensitivity. |
| ODAlarm.AlarmOutTime | char | Range is 10, 20, 40, 60, 30s, 1min , 2min. |
| ODAlarm.RecordDelayTime | char | Range is 10, 30, 1min, 2min, 5mins. 注：IPC不支持 |
| ODAlarm.AlarmOutManager | char | Alarm out switch. If only one alarm out, just use AlarmOutManager[0]. Four alarm out supported. |
| ODAlarm.EmailLink | char | Email link switch. 0: disable. 1: enable. |
| ODAlarm.RecordSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| ODAlarm.FtpUploadSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| ODAlarm.CloudSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |
| ODAlarm.PushSwitch | char | 0: disable. 1: enable. 注：IPC不支持 |

34. GeneralRec

34.1参数获取请求格式：

POST /action/getConfig/GeneralRec HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

34.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"ChnSwitch": 1,

"PreRecSwitch": 1,

"State": 1,

"Mode": 1,

"StreamMod": 0

},

{

"channel":2,

"ChnSwitch": 1,

"PreRecSwitch": 1,

"State": 1,

"Mode": 1,

"StreamMod": 0

}]

}

34.3参数设置请求格式：

POST /action/setConfig/GeneralRec HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和34.2中参数获取回应的jason格式一致

}

34.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

34.5 参数说明:

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Record.ChnSwitch | char | 0: close. 1: open. |
| Record.PreRecSwitch | char | 0: close. 1: open. 注：IPC不支持 |
| Record.State | char | Record automatically restored when power off restart. |
| Record.Mode | char | 0: Timer recording. 1: Boot recording. 注：IPC不支持 |
| Record.StreamMode | char | 0: mainstream. 1: substream. |

35. SmartRec

35.1参数获取请求格式：

POST /action/getConfig/SmartRec HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

35.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel" : [{

"channel":1,

"Type": 1

},

{

"channel":3,

"Type": 0

}]

}

35.3参数设置请求格式：

POST /action/setConfig/SmartRec HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和35.2中参数获取回应的jason格式一致

}

35.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

35.5 参数说明:

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| SmartRec.Type | char | Range is {0, 1}. 0: motion record 1: smart record |

36. Schedule

36.1参数获取请求格式：

POST /action/getConfig/Schedule HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [0xff,0xfd,0xfffff,0x12, 0xff,0xfd,0xf3,0x13]

}

36.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel" : [{

"channel":1,

"Schedule_0":"111111111111111111111111111111111111111111111111",

"Schedule_1":"111111111111111111111111111111111111111111111111",

"Schedule_2":"111111111111111111111111111111111111111111111111",

"Schedule_3":"000000000000000000000000000000000000000000000000",

"Schedule_4":"000000000000000000000000000000000000000000000000",

"Schedule_5":"000000000000000000000000000000000000000000000000",

"Schedule_6":"000000000000000000000000000000000000000000000000",

"RecordSchedule_0":"111111111111111111111111111111111111111111111111",

...

"RecordSchedule_6"::"111111111111111111111111111111111111111111111111",

"EmailSchedule_0"::"000000000000000000000000000000000000000000000000",

...

"EmailSchedule_6"::"111111111111111111111111111111111111111111111111"

},

{

"channel":2,

"Schedule_0":"FFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFF",

"Schedule_1":"FFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFF",

"Schedule_2":"FFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFF",

"Schedule_3":"000000000000000000000000000000000000000000000000",

"Schedule_4":"000000000000000000000000000000000000000000000000",

"Schedule_5":"000000000000000000000000000000000000000000000000",

"Schedule_6":"000000000000000000000000000000000000000000000000",

"RecordSchedule_0"::"FFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFF",

...

"RecordSchedule_6"::"111111111111111111111111111111111111111111111111",

"EmailSchedule_0"::"FFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFFF",

...

"EmailSchedule_6"::"111111111111111111111111111111111111111111111111"

}]

}

36.3参数设置请求格式：

POST /action/setConfig/Schedule HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和36.2中参数获取回应的jason格式一致

}

36.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

36.5 参数说明:

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Schedule[wd] RecordSchedule[wd] 注：IPC不支持 EmailSchedule[wd] 注：IPC不支持 | Char Char char | wd (week day) range is [0 ~ 6] (Sunday - Staurday) Bit 1: normal record schedule. Bit 2: motion record schedule. Bit 3: IO alarm record schedule. Bit 4: OSC record schedule. Bit 5: LCD record schedule. Bit 6:PID record schedule. 1 schedule，0:no schedule. wd (week day) range is [0 ~ 6] (Sunday - Staurday) Bit 1: normal record schedule. Bit 2: motion record schedule. Bit 3: IO alarm record schedule. Bit 4: OSC record schedule. Bit 5: LCD record schedule. Bit 6:PID record schedule. Bit:1 schedule，0:no schedule. wd (week day) range is [0 ~ 6] (Sunday - Staurday) Bit 1: normal email schedule. Bit 2: motion email schedule. Bit 3: IO alarm email schedule. Bit 4: OSC email schedule. Bit 5: LCD email schedule. Bit 6:PID email schedule. Bit:1 schedule，0:no schedule. |

37. System

37.1参数获取请求格式:

POST /action/getSysConfig/SystemInfo HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

37.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"LangUseFlag": 1,

"CurrentLang":1,

"VideoFormat":1,

"DateMode":0,

"TimeMode":0,

"Time":"2015-06-18_15:03:00",

"MaintainSwitch":1,

"MaintainPeriod1":0,

"MaintainPeriod2":1,

"MaintainTime":"03:00"

}

37.3参数设置请求格式：

POST /action/setSysConfig/SystemInfo HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和37.2中参数获取回应的jason格式一致

}

37.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

37.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| System.LangUseFlag | integer | Language flag of current usage, one bit represent a kind of language. |
| System.CurrentLang | char | Current system language. |
| System.VideoFormat | char | 0 - TS_PAL, 1 - TS_NTSC |
| System.DateMode | char | Date mode |
| System.TimeMode | char | Time mode. 0: 24 hours mode. 1: 12 hours mode. |
| System.Time | string | System time . Format: Year-month-Day_Hour:minute:Second . |
| System.MaintainSwitch | char | 0: close. 1: open. |
| System.MaintainPeriod1 | char | 0: every day. 1: every week. 2: every month. |
| System.MaintainPeriod2 | char | Some day in a week or some day in a month. |
| System.MaintainTime | string | Maintain time . Format: Hour:minute . |

38. User

38.1参数获取请求格式:

POST /action/getSysConfig/UserInfo HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

{

“UserNo”:1  //int 0 -6

}

## 38.2参数获取回应格式

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"UserNo": {

"UserNo": 1,

"UserName":"raysharp",

"Password":"519070,"

"PwdConfirm":"519070",

"SetRight":1,

"PreviewChannel":1,

"PlayBackChannel":1,

"BackupChannel":1,

"PlayBack":1,

"Backup":1,

"Preview":1,

"Switch":1,

"PwdSwitch":0,

"IsLive":1

}

}

38.3参数获取请求格式：

POST /action/getSysConfig/UserInfoAll HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

38.4参数获取请求格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"UserNo": [{

"UserNo": 1,

"UserName":"raysharp",

"Password":"519070,"

"PwdConfirm":"519070",

"SetRight":1,

"PreviewChannel":1,

"PlayBackChannel":1,

"BackupChannel":1,

"PlayBack":1,

"Backup":1,

"Preview":1,

"Switch":1,

"PwdSwitch":0,

"IsLive":1

},

{

"UserNo": 2,

"UserName":"raysharp",

"Password":"519070",

"PwdConfirm":"519070",

"SetRight":1,

"PreviewChannel":1,

"PlayBackChannel":1,

"BackupChannel":1,

"PlayBack":1,

"Backup":1,

"Preview":1,

"Switch":1,

"PwdSwitch":0,

"IsLive":1

}]

}

38.5参数设置请求格式：

POST /action/setSysConfig/UserInfo HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和38.4中参数获取回应的jason格式一致

}

38.6 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

38.7 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| User[UserNo].UserName | string | User name. Max length: 32. |
| User[UserNo].Password | string | User password. Max length: 32. |
| User[UserNo].PwdConfirm | string | User password conform. Max length: 32. |
| User[UserNo].SetRight | integer | Set right. Bitwise value. |
| User[UserNo].PreviewChannel | integer | Preview channel . |
| User[UserNo].PlayBackChannel | integer | Playback channel. |
| User[UserNo].BackupChannel | integer | Backup channel. |
| User[UserNo].PlayBack | char | Record playback right. |
| User[UserNo].Backup | char | Bakcup right |
| User[UserNo].Preview | char | Preview right. |
| User[UserNo].Switch | char | User in use. 0: not use. 1: in use. |
| User[UserNo].PwdSwitch | char | Login password switch. 0: close. 1: open. |
| User[UserNo].IsLive | char | User is on line. 0: off line. 1: on line. |

39. NTP

39.1参数获取请求格式:

POST /action/getSysConfig/NTP HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

39.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Switch":1,

"Serve":3,

"Port":13,

"SyncPeriod":31,

"TimeZone":8

}

39.3参数设置请求格式：

POST /action/setSysConfig/NTP HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和39.2中参数获取回应的jason格式一致

}

39.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

39.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| NTP.Switch | char | Enable/Disable NTP server. |
| NTP.Server | char | NTP server flag. |
| NTP.Port | short | Range is [1-65535]. Port of NTP server. 注：此参数IPC私有协议默认设置为13，IPC不支持 |
| NTP.SyncPeriod | short | Range is [0-65535], unit is minutes 注：实际上Range is [1-65535], unit is minutes |
| NTP.TimeZone | Char： | Range is [0-33]. 0: "GMT-12:00" 1: "GMT-11:00" 2: "GMT-10:00" 3: "GMT-09:00" 4: "GMT-08:00" 5: "GMT-07:00" 6: "GMT-06:00" 7: "GMT-05:00" 8: "GMT-04:30" 9: "GMT-04:00" 10: "GMT-03:30" 11: "GMT-03:00" 12: "GMT-02:00" 13: "GMT-01:00" 14： “GMT” 15: "GMT+01:00" 16: "GMT+02:00" 17: "GMT+03:00" 18: "GMT+03:30" 19: "GMT+04:00" 20: "GMT+04:30" 21: "GMT+05:00" 22: "GMT+05:30" 23: "GMT+05:45" 24: "GMT+06:00" 25: "GMT+06:30" 26: "GMT+07:00" 27: "GMT+08:00" 28: "GMT+09:00" 29: "GMT+09:30" 30: "GMT+10:00" 31: "GMT+11:00" 32: "GMT+12:00" 33: "GMT+13:00" |

40. DST

40.1参数获取请求格式:

POST /action/getSysConfig/DST HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

40.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"StartHour":"00:00:00",

"EndHour":"23:59:59",

"StartDate":"2015-04-12",

"EndDate":"2015-04-12",

"StartMonth":1,

"EndMonth":2,

"StartWeek":0,

"EndWeek":1,

"StartWeekDay":1,

"EndWeekDay":2,

"Switch":0,

"Mode":0,

"HaveDstTime":1,

"Offset":0

}

40.3参数设置请求格式：

POST /action/setSysConfig/DST HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和40.2中参数获取回应的jason格式一致

}

40.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

40.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| DST.StartHour | string | Dst start time. Format : hour:minute:second. |
| DST.EndHour | string | Dst end time. Format : hour:minute:second. |
| DST.StartDate | string | Dst start date. Format: year-month-day. |
| DST.EndDate | string | Dst end date. Format: year-month-day. |
| DST.StartMonth | char | Range is [0 ~ 11]. |

| DST.EndMonth | char | Range is [0 ~ 11]. |
| --- | --- | --- |
| DST.StartWeek | char | Range is {0, 1, 2, 3, 4}. 0: the first week, 1: the second week... |
| DSY.EndWeek | char | Range is {0, 1, 2, 3, 4}. 0: the first week, 1: the second week... |
| DST.StartWeekDay | char | Which day start from. 0-Sun, 1-Mon, ... 6-Sat |
| DST.EndWeekDay | char | Which day end of. 0-Sun, 1-Mon, ... 6-Sat |
| DST.Switch | char | Enable/Disable DST (daylight saving time) |
| DST.Mode | char | 0: Week. 1: Date. |
| DST.HaveDstTime | char | 0: not DST. 1: is DST. |
| DST.Offset |  | Dst offset value. 0: 1hour. 1: 2hour. |

41. Device

41.1参数获取请求格式:

POST /action/getSysConfig/DeviceInfo HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

41.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Name":"CH292H3_16M",

"ID":000000,

"Type":"IP CAMERA",

"HardwareVersion":"RS_CM_127B",

"SoftwareVersion":"V2.1.2.1_161010",

"IEClientVersion":"V1.0.3.20_160923",

"MACAddress":"D5-53-04-00-00-80"

}

41.3参数设置请求格式：

POST /action/setSysConfig/DeviceInfo HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和41.2中参数获取回应的jason格式一致

}

41.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

41.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Device.Name | string | Device name |
| Device.ID | Unsigned int | Device ID |
| Device.Type | string | Device type. |
| Device.HardwareVersion | string | Hardware version. |
| Device.SoftwareVersion | string | Software version |
| Device.IEClientVersion | string | IEClient version |
| Device.MACAddress | string | MAC address |

42. Device Storage

42.1参数获取请求格式:

POST /action/getSysConfig/DevStorage HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

42.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Redundancy:1,

"OverWriteSwitc":1,

"OverWritePeriod":6,

"OverWriteMode":1

}

42.3参数设置请求格式：

POST /action/setSysConfig/DevStorage HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和42.2中参数获取回应的jason格式一致

}

42.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

42.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Device.Redundancy | integer | Each bit represent a disk attribute. 0: main disk, 1: sub disk. 注：IPC不支持 |
| Device.OverWriteSwitch | char | 0:close, 1: open. 注：IPC不支持 |
| Device.OverWritePeriod | char | Overwrite period. unit is hour. 注：IPC不支持 |
| Device.OverWriteMode | char | Overwrite mode. 0: by hour, 1: by day. 注：IPC不支持 |

43. IP Filter

43.1参数获取请求格式:

POST /action/getSysConfig/IPFilter HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

43.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Switch":1,

"Filtered":[{

"FilterNo" : 0,

".IPAddress":"192.168.1.111",

"Enable":1

},

{

"FilterNo" : 1,

"IPAddress":"192.168.1.111",

"Enable":0

]}

}

43.3参数设置请求格式：

POST /action/setSysConfig/IPFilter HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和43.2中参数获取回应的jason格式一致

}

43.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

43.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| IPFilter.Switch | char | Enable/Disable access filter function. |
| IPFilter.Filtered[FilterNo ].IPAddress | string | Filtered IP address. Max length: 32. |
| IPFilter.Filtered[FilterNo ].Enable | char | Filtered IP address switch. 0: disable, 1: enable. |

44. ColorDefault

44.1请求格式:

POST /action/colorDefault HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

44.2回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Brightness":128,

"Contrast":128,

"Hue":128,

"Saturation":128,

"Sharpness":128

}

45. imageDefault

45.1请求格式:

POST /action/imageDefault HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

45.2回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"IRCutMode":0,

"IRCutDelay":2,

"IRCutSensitive":1,

"Mirro":0,

"Flip":0,

"Rotate":0,

"BackLightMode":1,

"BackLightLevel":1,

"R3dnrMode":1,

"R3dnrThreshTarget":128,

"DISEnable":1,

"DefogMode":1,

"DefogStrength":128,

"DwdrMode":1,

"DwdrStrength":128,

"GainControlMode":2,

"WBMode":0,

"Rgain":128,

"Ggain":128,

"Bgain":128,

"ShutterMode":0,

"ShutterSpeed":25,

"FlickerCtrl":0

}

46. Reboot

46.1请求格式:

POST /action/reboot HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

46.2回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

47. LoadDefault

47.1请求格式:

POST /action/loadDefault HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

"DisplayFlag": 1,

"RecordFlag": 1,

"NetworkFlag": 0,

"AlarmFlag": 1,

"DeviceFlag": 0,

"SystemFlag": 1,

"AdvanceFlag": 1

}

47.2回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

48. shot

48.1请求格式：

POST /action/snapshot HTTP/1.1

Host: 172.18.12.96

Content-Type: application/json

Authorization: Basic YWRtaW46

{

"snapTime":"2016-8-31T17:13:12Z",//optional

"channel":1,

"StreamType":1

}

48.2回应格式：

成功：

HTTP/1.1 200 OK

Connection: close

Content-Type:image/jpeg

Content-Length: xx

…..

失败：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "failed"，

"reason":"...."

}

48.3参数说明：

snapTime：抓拍的图片时间点，时间为设备的rtc时间，没有此项表示实时抓拍。

StreamType:  0:主码流、1:子码流

49. custom parameter

49.1保存参数请求格式：

POST /action/saveCustomParam HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-Length: xx

49.2 获取参数请求格式

Get /action/getCustomParam HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-Length: xx

…

49.3 回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Length: xx

{

"result": "failed"/"success",

"reason":"...."

}

50. AlarmOut

50.1 请求格式：

GET /action/AlarmOut HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

"action":  "string",   //"start"/"stop"

"channel" :  1

}

50.2 格式说明：

channel:表示通道号或者摄像机ID号

50.3 回应消息：

50.3.1成功回应

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"

}

50.3.2失败回应

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

51. ACCESSTKOEN

51.1请求格式：

POST /action/accesstoken/ HTTP/1.1

Host: 172.18.12.96

Content-Type: application/json

Authorization: Basic YWRtaW46

{

"accesstoken": "SADFDSFSDFSDA"

}

51.2 回应消息：

51.2.1成功回应

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"

}

51.2.2失败回应

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "failed"，// success , failed

"reason":"...."//如果是failed才有此项

}

52. 智能分析（获取Cross Counting 和 Line Crossing数据）

52.1请求格式：

POST /action/serachsmartcount/ HTTP/1.1

Host: 172.18.12.96

Content-Type: application/json

Authorization: Basic YWRtaW46

{

"startTime": "2018-3-16-13",

"endTime": "2018-3-16-15",

"alarmType": 1

}

52.2 回应消息：

52.2.1成功回应

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"alarmType":  1，

"times":  10

}

52.2.2失败回应

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "failed"，// success , failed

"reason":"...."//如果是failed才有此项

}

52.3 参数说明：

startTime: 开始时间   格式:  y-m-d-h

endTime：结束时间

alarmType：ANALYSIS_CC  = 0, //告警类型

ANALYSIS_PID = 1 ,

ANALYSIS_LCD    ,

ANALYSIS_SOD    ,

ANALYSIS_PD     ,

ANALYSIS_FD  = 5

times：对应报警类型发生的次数

53. OSDS

53.1参数获取请求格式：

POST /action/getConfig/OSDS HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: 50

{

"chmask": [2]

}

53.2参数获取回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"Channel":[{

"channel":1,

"OsdNo":[{

"OsdNo":0

"OSDSwitch":1,

"OSDType":0,

"Alpha":50,

"Content":["raysharp-ipc","123456"],

"PosX":20,

"PosY":20

},

{

"OsdNo":1,

"OSDSwitch":1,

"OSDType":0,

"Alpha":50,

"Content":["raysharp-ipc","66666"],

"PosX":20,

"PosY":20

}]

},

{

"channel":2

"OsdNo":[{

"OsdNo":0

"OSDSwitch":1,

"OSDType":0,

"Alpha":50,

"Content":["raysharp-ipc","123456"],

"PosX":20,

"PosY":20

},

{

"OsdNo":1,

"OSDSwitch":1,

"OSDType":0,

"Alpha":50,

"Content":["raysharp-ipc","123456"],

"PosX":20,

"PosY":20

}]

}]

}

53.3参数设置请求格式：

POST /action/setConfig/OSDS  HTTP/1.1

Host: 172.18.12.96

Authorization: Basic YWRtaW46

Content-type: application/json

Content-Length: xx

{

…//和53.2中参数获取回应的jason格式一致

}

53.4 参数设置回应格式：

HTTP/1.1 200 OK

Connection: close

Content-Type: application/json

Content-Length: xx

{

"result": "success"，// success , failed

"reason":"...."//如果是failed才有此项

}

53.5 参数说明：

| ParamName | ParamValue type | Description |
| --- | --- | --- |
| Osd[OsdNo].OSDSwitch | char | Osd switch. 0: disable ; 1: enable. |
| Osd[OsdNo].OSDType | char | Osd type. 0: time; 1: name. |
| Osd[OsdNo].Alpha | unsigned char | Transparency of overlaid osd, the smaller the value, the more transparent it will be. Range is [0 ~ 128]. 注：IPC IE实际上对应为Range is [1 ~ 128]. |
| Osd[OsdNo].Content | array | Content of overlaid osd. max: 20 elements, a element of Max length: 64. |
| Osd[OsdNo].PosX | integer | Osd postion. Top left x coordinate. |
| Osd[OsdNo].PosY | integer | Osd postion. Top left y coordinate. |