APOLLO simple manual

FUNCTIONS AND CHARCATERS

█　Full Aluminum body offer best heat radiation.

█　Remote control microphone with Wide angle Dot matrix LCD.

█　Multiple norms:

█　3 color display, Blue, Purple, Orange

█　Dual watch

█　Full channel scan

█　EMG Channel CH9/19

█　SQ and ASQ Control

█　4 Memory channels for each Norm

█　SQ, VOL, voltage level display

█　RX, TX, Field strength display

█　Keypad lock

█　VFO mode.

█　Optional earphone piece for Microphone

█　Optional remote PTT control cable.(Wired from microphone to wheel, to ensure safe driving)

9

█　KNOW ABOUT THIS RADIO                                                       17

12   11	13                      10

14	15                                      18

16

17

9

2	18

10		3

1

4	                                 5                12    11    13

6	      8

19

7

20

1… MEM/FRQ, Store channel or switch to VFO mode.

2… EMG/ M1: EMG CH9 and CH19, or program with other function.

3… DW/M2: Dual watch, or program with other function.

4… SC / M3: Channel scan, or program with other function.

5… AF / M4: AM/FM selection, or program with other function.

6… VOL+、Squelch level+ : Increase volume or Squelch level

7… VOL-、Squelch level- :  Decrease volume or Squelch level

8… COLOR: Change LCD backlight color, or Keypad lock.

9… PTT: Transmitting

10…SQ、VOL、ASQ

11…POW: Power key

12…UP: Channel UP.

13…DN: Channel down

14…TX indicator

15…RX indicator

16…LCD

17…Ext MIC/SP jack

18…Ext PTT cable jack

19…Mike

20…Speaker

█　HOW TO USE THIS RADIO:
1. Power on radio

① Hold[POW] key until LCD light on.

Note：When the radio in on, Hold [POW] key until LCD light off, the radio will power off.

② Adjust squelch level until you can hear background noise, refer to Page x about Squelch level setup.

③ Adjust volume level to wanted level, refer to Page x about Volume level setup.

2. Channel control

① Press [UP] or [DN] key to choose Channel

② Hold [UP] or [DN] key to choose channel fast.

Note：Before using, check if the working frequency and Norms are valid for using in your country.
If not, change the norms according to following instruction. The radio is defaulted set on EUH (AM/FM 4W)

The norms list see page x.

3. Choose Norms

① Power off radio

② Hold [A/F]+[POW] key until LCD light on.

③ Release [POW] key ，LCD displays BAND：ｘｘｘ

④ Release [A/F] key to enter norms menu.

⑤ Press [UP] or [DN] key to choose right norms

⑥ Hold [A/F] key to store and exit norm selection

4. Volume control

1-56 levels, Default level 53

① Press [SQ/VOL]key repeatedly，until LCD display VOL：XX

XX stands for volume level.

② Press [VOL＋] or  [VOL－] key to choose wanted volume level.

③ Hold [VOL＋] can fast increase volume level

④ Hold [VOL－]，can fast mute the speaker，LCD displays VOL：MT

In mute status, press [VOL＋] or [VOL－] key will resume to final volume level.

5. Squelch control

1-56 Levels，Default Level 11

① Choose a channel which is not busy.

② Press [SQ/VOL] key repeatedly until LCD displays SQ：XX

XX stands for Squelch level.

③ Press [VOL＋] or  [VOL－] key to choose wanted squelch level.

④ Hold [VOL＋] or [VOL－] can fast adjust squelch level.

⑤ Press [VOL－] key until the noise just appears，then press [VOL＋] until the noise just disappear，the squelch level setup is done.  The deeper squelch level chose, the stronger signal required to open the speaker and hear the calling.

6. ASQ control

① Hold [SQ/VOL] key until the LCD displays AQ，The ASQ function was turn on.

②  Repeatedly above function will switch between SQ、ASQ，in ASQ mode，SQ squelch level setup menu will disappear，and LCD displays SQ：AQ

7. LCD display

Dot matrix LCD display for channel number, frequency and operations.

2 Digits for display of channel number and Norms

5 Digits for display of frequency and Norms

FM　Mode

AM　Mode

SC：　Scan

键盘锁指示

VOL：53　Volume level

SQ：11　　Squelch level

MEM　　Storage

M1－M4　storage location

AQ： ASQ

DW：　Dual watch

1W/4W:　Power level

EMG：　　CH9/19

13.8：　　Current Voltage

RSI：　　RX signal strength.

PWR：　TX signal strength.

8. AM/FM mode

① Press [A/F] key to switch between AM/FM mode.

② Corresponding mode will displayed in the LCD.

9. Transmitting

① Hold [PTT]key

② TX LED indicator light on.

③ Hold the microphone about 2 cm away from your mouth and speaker in a normal tone.

④ Release [PTT]，the radio turn to RX mode ，TX LED indicator light off.

10. Receiving

The radio will keep in TX mode when it is not transmitting, the RX LED indicator will light on.

11. LCD color

Repeatedly press [COLOR] key，the background color for LED will change among orange, blue, purple.

12. EMG channel

① First press of [EMG] will choose CH9.

② The LCD displays EMG Icon

③Second press of [EMG] will choose CH19.

④Third press of [EMG] will resume to last none EMG channel.

13. Keypad lock

①To avoid mistake operation, hold [COLOR] will able to lock keys，

②The LCD displays XX icon

③Hold [COLOR] key again will unlock the keys.

14. Frequency mode

Hold [MEM] for over 5 seconds, the display will change to frequency mode.

Repeat hold [MEM] for over 5 seconds, the display will change to channel mode.

15. Scan

①Set SQ or ASQ first.

②Press [SC] key to start scanning，the LCD displays SC

③Press any key to stop scan ,，SC disappear.

16. Memory channel

In each norm, you can store 4 channels into M1, M2, M3, M4 for fast choose.

①Press[MEM] key，The MEM display and flash in LCD显示并闪烁

②Hold  memory channel key（M1, M2, M3,M4）until the MEM disappear

③The corresponding memory channel will show on LCD, the storage is done.

17. Using Memory Channel

①Press [MEM] key，MEM appears in LCD and flashes.

②Press the memory key （M1, M2 ,M3, M4）

③MEM disappear，the memory channel you chose will display in LCD.

18. DW channels

Two channels need be pre-stored for dual watch function.

①Adjust to first channel to be stored

②Hold [DW] key until DW in LCD flashes.

③Adjust to second channel to be stored]

④Hold [DW] key until DW flashes and disappear, the radio enter DW mode.

19: Using DW function

Press [DW] key, the DW in LCD flashes, the radio enter Dual watch mode.

20. Factory reset

①Hold [MEM] key，then hold [POW] key to power on radio

②Release [POW] key until LC displays “RE S”

③Release [MEM] key, the factory reset start.

④After full reset, the radio will automatically power off and power and start normal work.

█　Norms and Frequency

| Band ID | EU | EUH | CE | UK | PL | EU | I2 | DE | DEH |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Country | Europe | Europe | CEPT | UK | Poland | Italy/Spain | Italy | Germany | Germany |
| Power | AM=1W | AM=4W | / | / | AM=4W | AM=4W | AM=4W | AM=1W | AM=4W |
|  | FM=4W | FM=4W | FM=4W | FM=4W | FM=4W | FM=4W | FM=4W | FM=4W | FM=4W |
| CH-01 | 26.965 | 26.965 | 26.965 | 27.60125 | 26.960 | 26.965 | 26.965 | 26.965 | 26.565 |
| CH-02 | 26.975 | 26.975 | 26.975 | 27.61125 | 26.970 | 26.975 | 26.975 | 26.975 | 26.575 |
| CH-03 | 26.985 | 26.985 | 26.985 | 27.62125 | 26.980 | 26.985 | 26.985 | 26.985 | 26.585 |
| CH-04 | 27.005 | 27.005 | 27.005 | 27.63125 | 27.000 | 27.005 | 27.005 | 27.005 | 26.595 |
| CH-05 | 27.015 | 27.015 | 27.015 | 27.64125 | 27.010 | 27.015 | 27.015 | 27.015 | 26.605 |
| CH-06 | 27.025 | 27.025 | 27.025 | 27.65125 | 27.020 | 27.025 | 27.025 | 27.025 | 26.615 |
| CH-07 | 27.035 | 27.035 | 27.035 | 27.66125 | 27.030 | 27.035 | 27.035 | 27.035 | 26.625 |
| CH-08 | 27.055 | 27.055 | 27.055 | 27.67125 | 27.050 | 27.055 | 27.055 | 27.055 | 26.635 |
| CH-09 | 27.065 | 27.065 | 27.065 | 27.68125 | 27.060 | 27.065 | 27.065 | 27.065 | 26.645 |
| CH-10 | 27.075 | 27.075 | 27.075 | 27.69125 | 27.070 | 27.075 | 27.075 | 27.075 | 26.655 |
| CH-11 | 27.085 | 27.085 | 27.085 | 27.70125 | 27.080 | 27.085 | 27.085 | 27.085 | 26.665 |
| CH-12 | 27.105 | 27.105 | 27.105 | 27.71125 | 27.100 | 27.105 | 27.105 | 27.105 | 26.675 |
| CH-13 | 27.115 | 27.115 | 27.115 | 27.72125 | 27.110 | 27.115 | 27.115 | 27.115 | 26.685 |
| CH-14 | 27.125 | 27.125 | 27.125 | 27.73125 | 27.120 | 27.125 | 27.125 | 27.125 | 26.695 |
| CH-15 | 27.135 | 27.135 | 27.135 | 27.74125 | 27.130 | 27.135 | 27.135 | 27.135 | 26.705 |
| CH-16 | 27.155 | 27.155 | 27.155 | 27.75125 | 27.150 | 27.155 | 27.155 | 27.155 | 26.715 |
| CH-17 | 27.165 | 27.165 | 27.165 | 27.76125 | 27.160 | 27.165 | 27.165 | 27.165 | 26.725 |
| CH-18 | 27.175 | 27.175 | 27.175 | 27.77125 | 27.170 | 27.175 | 27.175 | 27.175 | 26.735 |
| CH-19 | 27.185 | 27.185 | 27.185 | 27.78125 | 27.180 | 27.185 | 27.185 | 27.185 | 26.745 |
| CH-20 | 27.205 | 27.205 | 27.205 | 27.79125 | 27.200 | 27.205 | 27.205 | 27.205 | 26.755 |
| CH-21 | 27.215 | 27.215 | 27.215 | 27.80125 | 27.210 | 27.215 | 27.215 | 27.215 | 26.765 |
| CH-22 | 27.225 | 27.225 | 27.225 | 27.81125 | 27.220 | 27.225 | 27.225 | 27.225 | 26.775 |
| CH-23 | 27.255 | 27.255 | 27.255 | 27.82125 | 27.250 | 27.255 | 27.255 | 27.255 | 26.785 |
| CH-24 | 27.235 | 27.235 | 27.235 | 27.83125 | 27.230 | 27.235 | 27.245 | 27.235 | 26.795 |
| CH-25 | 27.245 | 27.245 | 27.245 | 27.84125 | 27.240 | 27.245 | 27.265 | 27.245 | 26.805 |
| CH-26 | 27.265 | 27.265 | 27.265 | 27.85125 | 27.260 | 27.265 | 26.875 | 27.265 | 26.815 |
| CH-27 | 27.275 | 27.275 | 27.275 | 27.86125 | 27.270 | 27.275 | 26.885 | 27.275 | 26.825 |
| CH-28 | 27.285 | 27.285 | 27.285 | 27.87125 | 27.280 | 27.285 | 26.895 | 27.285 | 26.835 |
| CH-29 | 27.295 | 27.295 | 27.295 | 27.88125 | 27.290 | 27.295 | 26.905 | 27.295 | 26.845 |
| CH-30 | 27.305 | 27.305 | 27.305 | 27.89125 | 27.300 | 27.305 | 26.915 | 27.305 | 26.855 |
| CH-31 | 27.315 | 27.315 | 27.315 | 27.90125 | 27.310 | 27.315 | 26.925 | 27.315 | 26.865 |
| CH-32 | 27.325 | 27.325 | 27.325 | 27.91125 | 27.320 | 27.325 | 26.935 | 27.325 | 26.875 |
| CH-33 | 27.335 | 27.335 | 27.335 | 27.92125 | 27.330 | 27.335 | 26.945 | 27.335 | 26.885 |
| CH-34 | 27.345 | 27.345 | 27.345 | 27.93125 | 27.340 | 27.345 | 26.955 | 27.345 | 26.895 |
| CH-35 | 27.355 | 27.355 | 27.355 | 27.94125 | 27.350 | 27.355 | 26.855 | 27.355 | 26.905 |
| CH-36 | 27.365 | 27.365 | 27.365 | 27.95125 | 27.360 | 27.365 | 26.865 | 27.365 | 26.915 |
| CH-37 | 27.375 | 27.375 | 27.375 | 27.96125 | 27.370 | 27.375 |  | 27.375 | 26.925 |
| CH-38 | 27.385 | 27.385 | 27.385 | 27.97125 | 27.380 | 27.385 |  | 27.385 | 26.935 |
| CH-39 | 27.395 | 27.395 | 27.395 | 27.98125 | 27.390 | 27.395 |  | 27.395 | 26.945 |
| CH-40 | 27.405 | 27.405 | 27.405 | 27.99125 | 27.400 | 27.405 |  | 27.405 | 26.955 |

█　Specification

| GENERAL |
| --- |
| Modulation modes | AM/FM |
| Frequency ranges | 26.565-27.99125MHZ |
| Frequency Tolerance | 0.005% |
| Input Voltage | 13.2V |
| Dimensions(in mm) |  |
| Weight |  |
| Frequency Control | PLL Synthesizer |
| Operating Temperature Range | -20° C TO + 55° C |
| Current Drain | Transmit:1.4A MAX Receive: Squelched 0.4A, VOL Max: 1.3A |
| Antenna Connector | UHF,SO-239 |
| TRANSMITTER |
| Output power | 4 Watt FM 1/4Watt AM |
| Transmission interference | inferior to 4nW(-54dBm) |
| Frequency Response | 300-3000Hz |
| Modulated signal distortion | inferior to 5% |
| Output Impedance | 50 ohms |
| RECEPTION |
| Sensitivity | Less than 1uV for 10dB(S+N)/N |
| Image Rejection | 70dB |
| Adjacent channel selectivity | 60dB |
| IF Frequencies | 1st 10.695MHz 2nd 455KHz |
| Automatic Gain Control(AGC) | Less than 10dB change in audio Output for inputs from 10 to 50000uV |
| Squelch | less than 1uV |
| Audio Output Power | 2Watts |
| Frequency Response | 300-3000Hz |