jpeg html page

http://dvr-ip/m.html

SNAPSHOT

jpeg single channel cgi

http://dvr-ip/cgi-bin/net_jpeg.cgi?ch=0

ch: 0~31

MOTION JPEG

jpeg multi channels cgi

http://dvr-ip/cgi-bin/net_jpeg.cgi?push=1&ch=15

ch: bits

ex:

ch=1 -> ch1,

ch=3 -> ch1 and ch2,

ch=15 -> ch1, ch2, ch3, ch4.

raw data:

jpeg data,

frame_head_t,

jpeg data,

frame_head_t

video/audio live

http://dvr-ip/cgi-bin/net_video.cgi?hq=0&iframe=65535&pframe=65535&audio=65535

hq: 0(low quality), 1(high quality)

iframe: bits

pframe: bits

audio: bits

Packet Format:

head_t

frame_head_t

h.264 raw data ( Video / Audio )